## Slide 1: N.C. Department of Labor OSH Division
Asbestos Standards
- 29 CFR 1926.1101
- 29 CFR 1910.1001
Notes: Rev 0: 6/24/2013
START WITH REMINDER OF LEAD AT HOME
http://www.icij.org/project/dangers-dust/map-top-asbestos-producers-and-consumers

## Slide 2: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101)

## Slide 3: Scope and Application
Covers asbestos exposure in all work as defined in 1910.12(b) 1926.10(a), regardless of the type of worksite or location
  “Construction work" means work for construction, alteration, and/or repair, including painting and decorating.
    Definition’s Source: 29 CFR 1910.12(b)
    1926.10(a), and/or OSHA Dictionary
29 CFR 1926.1101(a)
Notes: Definition of Construction Work is from OSHA Dictionary

## Slide 4: Scope and Application
Includes but is not limited to:
  Demolition or salvage of structures
  Removal or encapsulation of materials
  Construction, alteration, repair, maintenance, or renovation
  Installation of products containing asbestos
  Spill/emergency clean-up
  Transportation, disposal, storage, containment and housekeeping activities on the site where construction activities are performed
Does not apply to asbestos-containing asphalt roof coatings, cements and mastics
29 CFR 1926.1101(a)
Notes: Question: Why doesn’t the scope and application apply to asbestos-containing asphalt roof coatings, cements and mastics?
Answer: Because asbestos-containing asphalt roof coatings, cements and mastics are considered Category I nonfriable asbestos-containing material (ACM). Category I nonfriable ACM is a NESHAP term.

## Slide 5: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101)

## Slide 6: Definitions
Asbestos
  Chrysotile, amosite, crocidolite, tremolite asbestos, anthophyllite asbestos, actinolite asbestos, and any of these minerals that have been chemically altered; includes PACM
ACM
  “Asbestos-containing material,” any material containing >1% asbestos
PACM
  “Presumed asbestos-containing material”
29 CFR 1926.1101(b)

## Slide 7: Additional Definitions
Friable
  Any materials that contain more than 1% asbestos and can be crumbled, pulverized, or reduced to powder by hand pressure when dry.
Nonfriable
  Any materials that contain more than 1% asbestos and that can not be crumbled, pulverized, or reduced to powder by hand pressure when dry.

## Slide 8: Examples
Notes: Question: Friable or Nonfriable
Answer: TSI runs are friable. The elbows and joints maybe nonfriable.

## Slide 9: Examples
Notes: Question: Friable or Nonfriable
Answer: Mastics, cements, coatings are usually nonfriable

## Slide 10: Examples
Notes: Question: Friable or Nonfriable
Answer: Transite™ (cementitious asbestos) panels are nonfriable unless damaged during removal.

## Slide 11: Examples
Notes: Question: Friable or Nonfriable
Answer: The ACM on the floor would be considered friable.
The ACM plaster would also be considered friable due to damage incurred while removing the wall paper.

## Slide 12: Examples
Notes: Question: Friable or Nonfriable
Answer: 9” X 9” ACM floor tiles are nonfriable (unless damaged)

## Slide 13: Definitions
Critical Barrier
  One or more layers of plastic sealed over all openings into a work area or
    Any other similarly placed physical barrier
    To prevent airborne asbestos in a work area from migrating to an adjacent area.
Surfacing Material
  Material that is sprayed-on, troweled-on, or otherwise applied to surfaces
Thermal System Insulation (TSI)
  ACM applied to pipes, fittings, boilers, breeching, tanks, ducts or other structural components to prevent heat loss or gain
29 CFR 1926.1101(b)

## Slide 14: Definitions
Disturbance
  Activities that:
    Disrupt the matrix of ACM or PACM,
    Crumble or pulverize ACM or PACM, or
    Generate visible debris from ACM or PACM
    Includes cutting away small amounts of ACM and PACM, ≤ amount contained in one standard-sized glove bag or waste bag in order to access a building component
29 CFR 1926.1101(b)
Notes: > 1 std glove bag or waste bag places Class III removal of TSI or SM into Class I operation.

## Slide 15: Definitions
Class I Asbestos Work
  Activities involving the removal of TSI or surfacing ACM and PACM
Class II Asbestos Work
  Activities involving the removal of ACM which is not TSI or surfacing material (also
  known as Miscellaneous ACM)
    Examples: removal of asbestos-containing
    wallboard, floor tile, and roofing shingles
29 CFR 1926.1101(b)

## Slide 16: Definitions
Class III Asbestos Work (also known as O&M)
  Repair and maintenance operations where ACM and/or PACM is likely to be disturbed
  Where is this work?
29 CFR 1926.1101(b)
Notes: Class III work includes maintenance work for which a small amount of ACM must be cut away to access mechanical or structural components of buildings. In order to qualify as Class III work (rather than Class I or Class II work), the amount cut away must be less than the amount that can be contained in a standard-sized glove bag or waste bag.

## Slide 17: Definitions 29 CFR 1926.1101(b)
VS.
Notes: Standard Glovebag vs. Large Glovebag

## Slide 18: Definitions 29 CFR 1926.1101(b)
Class IV Asbestos Work
  Maintenance and custodial activities during which employees contact but do not disturb ACM or PACM and activities to clean up dust, waste and debris resulting from Class I, II, and III activities

## Slide 19: Definitions
Building/Facility Owner
Intact
  ACM that has not crumbled, been pulverized, or otherwise deteriorated
29 CFR 1926.1101(b)

## Slide 20: Definitions
Competent Person
  Big definition
29 CFR 1926.1101(b)
Notes: Required Training:
Class III Worker- 2-Hour Asbestos Awareness plus 14 Hours of Additional Training
Class IV Worker- 2-Hour Asbestos Awareness
  Can identify existing asbestos hazards in the workplace and select appropriate control strategy for asbestos exposure and
  Has authority to take prompt corrective action to eliminate them; and
  For Class I and II work: trained in a training course that meets the criteria of EPA’s Model Accreditation Plan for supervisors, or its equivalent (40 CFR 763 AHERA)
  For Class III and IV work: is specially trained including a course meeting EPA requirements for training of local education agency maintenance and custodial staff (40 CFR 763.92(a)(2) AHERA)

## Slide 21: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101(c)
29 CFR 1926.1101(c)

## Slide 22: Permissible Exposure Limits
Time-Weighted Average Limit
  0.1 fiber/cubic centimeter as an 8-hour TWA (0.1 f/cc)
Excursion Limit
  1.0 fiber/cubic centimeter as averaged over 30 minutes
29 CFR 1926.1101(c)
Notes: Excursion limit still counted as part of TWA

## Slide 23: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101(d)

## Slide 24: Multi-Employer Worksites
Employer whose work requires a regulated area shall inform other employers of:
  Nature of such work
  Existence /of and requirements for regulated areas
  Other employers are not exposed
Abatement shall be by contractor who
creates or controls source of contamination
29 CFR 1926.1101(d)

## Slide 25: Multi-Employer Worksites
D1
D4 ????? You want me to do what?
D5
29 CFR 1926.1101(d)

## Slide 26: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101(e)

## Slide 27: Regulated Areas
Class I, II, and III asbestos work
All other operations where PEL is or may reasonably be exceeded
29 CFR 1926.1101(e)
Notes: “Regulated area”: an area established by the employer to demarcate areas where Class I, II, and III asbestos work is conducted, and any adjoining area where debris and waste from such asbestos work accumulate; and a work area within which airborne concentrations of asbestos, exceed or there is a reasonable possibility they may exceed the permissible exposure limit. Requirements for regulated areas are set out in paragraph (e) of this section.

## Slide 28: Regulated Areas
Demarcated in any effective manner
  Critical barriers or negative pressure enclosures may be used
  Signs must be provided
Limited access
Respirators to be provided
Supervised by competent person
29 CFR 1926.1101(e)
Notes: Access limited to persons authorized by employer or OSH Act

## Slide 29: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101(f)

## Slide 30
REALLY???!!!
More like what I used!
Notes: Now let’s discuss the requirements for exposure assessments and monitoring

## Slide 33: Exposure Assessments and Monitoring
General Requirements
  For each workplace/operation where monitoring is required under this section:
  Must be a representative 8-hr TWA
  30-min EL samples (1.0f/cc) highest exposure tasks
  Competent person must conduct the exposure assessment
29 CFR 1926.1101(f)(1)
Notes: EL = Excursion Limit
Samples collected on filter and analyzed by PCM
Purpose of assessment by competent person: to ensure appropriate control systems are applied

## Slide 34: Exposure Assessments and Monitoring
  Initial Exposure Assessment
    Must conduct assessment before or at the initiation of the operation to ascertain expected exposures
    Triggered by exposure data or lack of a “negative exposure assessment”
29 CFR 1926.1101(f)(2)

## Slide 35: Exposure Assessments and Monitoring
  Basis of Initial Monitoring
    Monitoring shall be conducted as per 1926.1101(f)(1)(iii)
1101(f)(2)(i)

## Slide 36: Exposure Assessments and Monitoring
  For Class I Work the employer shall presume that employees are exposed in excess of the TWA and EL unless
      Documented initial exposure monitoring demonstrates employees will not be exposed in excess of the PELs, or
      The employer completes a negative exposure assessment as per 1926.1101(f)(2)(iii)
29 CFR 1926.1101(f)(2)

## Slide 37: Negative Exposure Assessment
“Negative Exposure Assessment” required to conclude that exposures are likely to be consistently less than PELs
29 CFR 1926.1101(f)(2)
Notes:   (Oh yeah, 8 hours = 480 minutes)

## Slide 38: Negative Exposure Assessment
Objective data that product, mineral, or activity cannot release airborne fibers in concentrations > PELs under the most severe conditions
Monitoring data obtained w/in prior 12 months for work operations/conditions “closely resembling” current operations and were conducted by employees no more trained/experienced than current employees
Results of initial exposure monitoring of the current job
29 CFR 1926.1101(f)

## Slide 39: Periodic Monitoring
Class I and II work in a regulated area: daily representative monitoring unless employer has NEA for the entire operation
All other operations: periodic monitoring sufficient to document the exposure
29 CFR 1926.1101(f)
Notes: Exception: Employees doing Class I work who are using a control listed in (g)(4)(i), (ii), or (iii) and employees doing Class II work may be equipped with supplied-air respirators operated in the positive-pressure mode in lieu of daily monitoring

## Slide 40: Termination of Monitoring
May discontinue monitoring if exposures < PELs
Additional monitoring is required when change may produce exposures > PELs
  Process
  Control equipment
  Personnel
  Work practice
29 CFR 1926.1101(f)

## Slide 41: Termination of Monitoring
Observation of monitoring by employees and their designated representatives
Affected employees notified of the monitoring results, in writing or by posting

## Slide 42: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101(g)

## Slide 43
Notes: Now let’s discuss paragraph (g) - methods of compliance

## Slide 44: Methods of Compliance
All asbestos work: Regardless of level of exposure
  Vacuum cleaners with HEPA filters
  Wet methods or wetting agents during handling, mixing, removal, cutting, application, and cleanup
  Prompt cleanup and disposal of wastes and debris in leak-tight containers
29 CFR 1926.1101(g)
Notes:   see (g)(8)(ii) for roofing exceptions
  UNLESS INFEASIBLE – wet methods.. Where?

## Slide 45: Methods of Compliance
Engineering controls and work practices to achieve PELs
  LEV with HEPA filter dust collection system
  Enclosing/isolating processes producing asbestos dust
29 CFR 1926.1101(g)
Notes: LEV = local exhaust ventilation

## Slide 46: Methods of Compliance
PROHIBITIONS
  High-speed abrasive disc saws
  Compressed air
  Dry sweeping, shoveling, or other cleanup
  Employee rotation
29 CFR 1926.1101(g)

## Slide 47: Methods of Compliance
Class I Jobs
  Critical barriers to prevent the migration of airborne asbestos from the regulated area
  Containment
29 CFR 1926.1101(g)

## Slide 48: Methods of Compliance
Class I Jobs - Specific control methods required:
  >25 linear or 10 square feet of TSI or surfacing material
  For all other Class I jobs where there is no negative exposure assessment
  For Class I jobs where employees are working in areas adjacent to the regulated
  area
29 CFR 1926.1101(g)
Notes: Next slide

## Slide 49: Methods of Compliance
Class I Jobs
  Isolation of HVAC systems (double layer of 6 mil plastic or equivalent)
  Impermeable dropcloths beneath removal activity
29 CFR 1926.1101(g)

## Slide 50: Methods of Compliance
  Cover all objects within regulated area with impermeable materials
  Where no NEA, or > PEL, ventilation of the regulated area to move air from the employee’s breathing zone toward HEPA-filtered collection device

## Slide 51: Methods of Compliance
Class I Jobs
  One or more of the following specific control methods shall be used:
    Negative Pressure Enclosure (NPE) Systems
    Glove Bag Systems
    Negative Pressure Glove Bag Systems
    Negative Pressure Glove Box Systems
    Water Spray Process System
    Small walk-in enclosure accommodating
    1 - 2 persons, if the project can be
    completely contained in the enclosure
29 CFR 1926.1101(g)
Notes:   Negative Pressure Enclosure (NPE) Systems, where work area configuration does not make erection infeasible
  Glove Bag Systems, for removal of PACM and/or ACM from straight runs of piping, elbows, and other connections
  Negative Pressure Glove Bag Systems, for removal of ACM or PACM from piping
  Negative Pressure Glove Box Systems, for removal of ACM or PACM from pipe runs
  Water Spray Process System, for removal of ACM and PACM from cold line piping, where employees have completed a separate 40-hour training course in its use

## Slide 52: Methods of Compliance
Class II Jobs
  Supervision by competent person, and when:
    No NEA; or
    May be > PELs; or
    ACM not removed in substantially intact state
  Critical barriers
  Impermeable drop-cloths
29 CFR 1926.1101(g)
Notes: If other barrier or isolation method, must be verified by perimeter monitoring or clearance monitoring.

## Slide 53: Methods of Compliance
Removal of vinyl and asphalt flooring materials which contain ACM or for which in buildings constructed ≤ 1980, the employer has not verified the absence of ACM
Removal of roofing material
Removal of cementitious asbestos-containing siding and shingles or transite panels
Removal of gaskets
Performing any other Class II removal
Installation, removal, or repair of intact bituminous/resinous encapsulated roofing materials (mastics, flashings, etc.) and asphaltic pipeline wraps
29 CFR 1926.1101(g)
Notes: Talk about dates
Discuss settlement agreements for roofing and flooring.
Also, public sector has to deal with ruptured asbestos-containing cementitious water pipes

## Slide 54: Methods of Compliance
Class I methods may also be used for Class II work, except that glove bags and glove boxes are allowed if they fully enclose the Class II material to be removed
Alternative controls may be used if they comply with the following:
  Data representing exposure will not exceed the PELs
  A competent person evaluates and certifies such controls
29 CFR 1926.1101(g)
Notes: Note: competent person may evaluate alternative control; CIH or PE not required.

## Slide 55: Methods of Compliance
Class III Jobs
  Wet methods
  LEV, to the extent feasible
29 CFR 1926.1101(g)

## Slide 56: Methods of Compliance
Drilling, cutting, abrading, sanding, chipping, breaking, or sawing TSI or surfacing material
  Impermeable dropcloths and mini-enclosures or
  Glove bag systems or another isolation method
No NEA or > PELs
  Impermeable dropcloths and plastic barriers or
  Isolation using a control system specified for Class I jobs
Where
  TSI or surfacing material involved or
  No NEA, or > PELs
  Respiratory protection required according to paragraph (h)
29 CFR 1926.1101(g)

## Slide 57: Methods of Compliance
Class IV Jobs
  Trained per paragraph (k)(9)
  respirators are required / then they shall wear respirators
  Waste and debris in areas where
  friable TSI or surfacing material is
  accessible assumed to contain
  asbestos
29 CFR 1926.1101(g)

## Slide 58: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101(h)

## Slide 59
Notes: Discuss respiratory protection, protective clothing and hygiene facilities

## Slide 60: Respiratory Protection
Must be provided and used for:
  Class I jobs
  Class II jobs where ACM is not removed substantially intact
  Class II and III jobs not performed using wet methods; exception: sloped roofs
  Class II and III jobs where no NEA
  Class III jobs where TSI or surfacing material ACM or PACM is disturbed
  Class IV work in regulated areas where employees performing other work are required to wear respirators
  > PELs
  Emergencies
29 CFR 1926.1101(h)

## Slide 61: Respirator Selection
Employers shall provide respirators per Table 1
NIOSH approved
Tight-fitting, PAPR shall be provided in lieu of any negative-pressure respirator whenever
  Employee chooses to use this type of respirator and
  Respirator will provide adequate protection
29 CFR 1926.1101(h)
Notes: PAPR = powered-air purifying respirator

## Slide 62: Table 1 Respiratory Protection for Asbestos Fibers
Airborne concentration of asbestos or conditions of use | Required respirator
Not in excess of 1 f/cc (10 x PEL) or otherwise as required independent of exposure pursuant to paragraph (h)(2)(iv) of this section. | Half–mask air purifying respirator other than a disposable respirator, equipped with high-efficiency filters.
Not in excess of 5 f/cc (50 x PEL). | Full facepiece air–purifying respirator equipped with high efficiency filters.
Not in excess of 10 f/cc (100 x PEL). | Any powered air–purifying respirator equipped with high efficiency filters or any supplied air respirator operated in continuous flow mode.
Not in excess of 100 f/cc (1,000 x PEL) or unknown concentration. | Full facepiece supplied air respirator operated in pressure demand mode.
Greater than 100 f/cc (1,000 x PEL) or unknown concentration. | Full facepiece supplied air respirator operated in pressure demand mode, equipped with an auxiliary positive pressure self–contained breathing apparatus.
Notes: Should be replaced with 1910.134 table on PELs

## Slide 63: Respirator Selection
Half-mask APR (not disposable!) with HEPA filters
  Class II and III jobs where no NEA
  Class III jobs where TSI or SM being disturbed
Tight fitting PAPRs with HEPA filters or full-facepiece supplied air respirators operated in pressure-demand mode, with HEPA egress cartridges or an auxiliary positive pressure SCBA, required for Class I work where:
  NEA has not been produced, and
  Exposure assessment levels are ≤ 1 fiber/cc (8-hour TWA)
29 CFR 1926.1101(h)

## Slide 64: Respirator Selection
Full-facepiece SAR operated in PD mode equipped with an aux. positive pressure SCBA, required for Class I work where
  NEA has not been produced, and
  Exposure assessment levels are > 1f/cc for an 8-hour TWA
29 CFR 1926.1101(h)
Notes: SAR = supplied air respirator
Reminder: Exposure assessment assumed > PELs for Class I work until initial exposure monitoring done

## Slide 65: Respirator Selection
Comply with 1910.134(b)-(d) (not (d)(1)(iii)), (f), and (m)
Permitted to change filters whenever an increase in breathing resistance is detected
Permitted to leave work areas to wash their faces and respirator facepieces whenever necessary to prevent skin irritation
29 CFR 1926.1101(h)
Notes: 1910.134(b): definitions
1910.134(c): respiratory protection program
1910.134(d): selection of respirators; (d)(1)(iii) refers to identification of hazards and determination of exposure levels
1910.134(e): medical evaluation
1910.134(f): fit testing
1910.134(m): recordkeeping

## Slide 66: Respirator Selection
Comply with 1910.134(b)-(d) (not (d)(1)(iii)), (f), and (m)
Permitted to change filters whenever an increase in breathing resistance is detected
Permitted to leave work areas to wash their faces and respirator facepieces whenever necessary to prevent skin irritation
The employer shall identify and evaluate the respiratory hazard(s) in the workplace; this evaluation shall include a reasonable estimate of employee exposures to respiratory hazard(s) and an identification of the contaminant's chemical state and physical form. Where the employer cannot identify or reasonably estimate the employee exposure, the employer shall consider the atmosphere to be IDLH.
29 CFR 1926.1101(h)
Notes: 1910.134(b): definitions
1910.134(c): respiratory protection program
1910.134(d): selection of respirators; (d)(1)(iii) refers to identification of hazards and determination of exposure levels
1910.134(e): medical evaluation
1910.134(f): fit testing
1910.134(m): recordkeeping

## Slide 67: Respirator Selection
No employee will be assigned to tasks requiring respirators if an examining physician finds:
  Employee cannot function normally wearing a respirator or
  Will endanger him/herself or others
Employees not approved for respirator use may transfer to another job if available
29 CFR 1926.1101(h)

## Slide 68: Respirator Fit Testing
Fit tests for negative pressure respirators
  Initial fitting and
  At least annually thereafter
QLFT may be used only for:
  Half-mask respirators or
  Full-facepiece air-purifying respirators worn in lieu of half-facepiece APR
QLFT and QNFT conducted per
Appendix C
29 CFR 1926.1101(h)

## Slide 69: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101(i)

## Slide 70: Protective Clothing
Coveralls, head coverings, gloves, and foot coverings are required for:
  Employee exposure > PELs
  Employees doing work for which required NEA not produced
  Employees performing Class I work involving removal of > 25 linear or 10 sq. ft. of TSI or surfacing ACM or PACM
Laundering of contaminated clothing must be done so as to prevent exposures > PELs
Employers must inform launderers of the requirement to prevent release of airborne asbestos > PELs
29 CFR 1926.1101(i)

## Slide 71: Protective Clothing
Contaminated clothing must be transported in labeled, sealed impermeable bags or containers
Competent person must examine worksuits at least 1x per workshift for rips or tears
Rips/tears must be immediately mended, or the worksuit replaced
29 CFR 1926.1101(i)

## Slide 72: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101(j)

## Slide 73: Hygiene Facilities
Class I Jobs > 25 Lin. Ft. or 10 Sq. Ft. of TSI or Surfacing ACM and PACM
  Decontamination area adjacent and connected to the regulated area
    Equipment room
    Shower area (adjacent to equipment room and clean room)
    Clean change room
  Employees must enter the regulated area through the decon area
    Clean room  Shower area  Equipment room
  Employees must exit the regulated area through the decon area
    Equipment room  Shower area  Clean room
  For all Class I work: Lunch areas must be provided in areas in which airborne asbestos concentration is < PELs
29 CFR 1926.1101(j)
Notes: [Note: check on significance of 25 linear ft and 10 sq. ft.]

## Slide 74: Hygiene Facilities
Other Class I Jobs, Class II Jobs, and Class III Jobs
  Must establish an equipment room or area adjacent to the regulated area for the decontamination of employees and equipment
  Employees must enter and exit the regulated area through the equipment room or area
29 CFR 1926.1101(j)

## Slide 75: Hygiene Facilities
Class IV Jobs
  Hygiene facilities and practices must match those of employees performing higher classification work within the same regulated area, or
  Decontamination facilities specified for “Other Class I Jobs, Class II Jobs, and Class III Jobs” must be provided for employees cleaning up debris and material identified as TSI or surfacing ACM or PACM
  For all jobs covered under this standard: smoking is not permitted where there is exposure to asbestos
29 CFR 1926.1101(j)

## Slide 76: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101(k)

## Slide 77: Communication of Hazards
Duties of Building and Facility Owners
  Identify presence, location, and quantity of ACM/PACM, including:
    TSI and sprayed on/troweled-on surfacing materials in buildings or substrates constructed ≤ 1980
    Resilient flooring material installed ≤ 1980
29 CFR 1926.1101(k)
Notes: Identify ACM/PACM before work begun

## Slide 78: Communication of Hazards
Duties of Building and Facility Owners
  Notification of:
    Presence, location, and quantity of ACM/PACM
  To:
    Prospective employers applying for/bidding for work
    Employees of owner who will work in or adjacent to areas containing such materials
    All employers on multi-employer worksites whose employees will be performing work within or adjacent to areas containing such materials
    Tenants who will occupy areas containing such materials
29 CFR 1926.1101(k)
Notes: Identify ACM/PACM before work begun

## Slide 79: Communication of Hazards
Duties of Building and Facility Owners
  Post signs at entrance to mechanical rooms/areas which contain ACM and/or PACM
  Identify material present, its location, work practices to avoid disturbance
  Post signs or labels on previously installed ACM/PACM to inform employees of which materials are affected
29 CFR 1926.1101(k)
Asbestos

## Slide 80: Communication of Hazards
Duties of Employers
  Before work, identify presence, location, and quantity of ACM/PACM
Before work, inform following persons of the location and quantity of ACM/PACM and the precautions to be taken to confine airborne asbestos
  Owners of building/facility
  Employees who will perform work and
  employers of employees who work and/or
  will be working in adjacent areas
29 CFR 1926.1101(k)

## Slide 81: Communication of Hazards
Duties of Employers
  Within 10 days of completion, inform building/facility owner and employers of employees who will be working in the area
  Current location and quantity of ACM/PACM remaining
  Final monitoring results
Within 24 hrs of discovering ACM/PACM on a worksite, must convey presence, location, and quantity of such newly-discovered materials to:
  Owner
  Other employers of employees working at worksite
Post signs or labels on previously installed ACM/PACM to inform employees of which materials are affected
29 CFR 1926.1101(k)

## Slide 82: Communication of Hazards
Criteria to Rebut the Designation of PACM
  Having an AHERA inspection
Performing tests that demonstrate that the material is not ACM
  Collection of bulk samples following requirements of 40 CFR 763.86
  Performed by an accredited inspector or CIH
  Analysis of samples by persons/laboratories participating in nationally-recognized testing programs or round robin testing program
  For flooring materials, a determination by an IH based on recognized analytical techniques
29 CFR 1926.1101(k)

## Slide 83: Communication of Hazards
Criteria to Rebut the Designation of PACM
  Data and information must be maintained for as long as they are relied on to rebut the presumption
29 CFR 1926.1101(k)

## Slide 84: Communication of Hazards
Signs
  Warning signs must be used to demarcate regulated areas
Wording for signs:
Additional wording where applicable:
  “RESPIRATORS AND PROTECTIVE
  CLOTHING ARE REQUIRED IN THIS AREA”
29 CFR 1926.1101(k)

## Slide 85: Communication of Hazards
Labels required on:
  Products containing asbestos
  Containers containing such products, including waste containers
  Installed asbestos products, where feasible, including previously installed material identified as ACM/PACM
29 CFR 1926.1101(k)

## Slide 86: Communication of Hazards Labels
Exemptions from labeling include:
  Products where asbestos fibers have been modified by a bonding agent, coating, binder, or other material, if no concentration of fibers PELs will be produced during any reasonably foreseeable use, handling, etc.
  Products where asbestos is < 1.0% by weight
  Installed materials where signs providing same information are posted
29 CFR 1926.1101(k)

## Slide 87: Communication of Hazards Labels
Wording on labels
Labels must also contain a warning statement against breathing asbestos fibers
DANGER
CONTAINS ASBESTOS FIBERS
AVOID CREATING DUST
CANCER AND LUNG DISEASE HAZARD
29 CFR 1926.1101(k)

## Slide 88: Employee Information and Training General Requirements
Provided prior to or at time of initial assignment
Annually
Manner comprehensible to employee
29 CFR 1926.1101(k)

## Slide 89: Employee Information and Training Basic Information
How to recognize asbestos, including PACM
Health effects
Relationship between smoking and asbestos in producing lung cancer
Operations that could result in exposure and protective measures and their use, as applicable
For Class III and IV work, information equivalent to the contents of EPA 20T-2003, “Managing Asbestos In-Place”
Purpose, proper use, fitting instructions, and limitations of respirators
29 CFR 1926.1101(k)

## Slide 90: Employee Information and Training Basic Information
Appropriate work practices for the job
Medical surveillance program requirements
Content of standard, including appendices
Names, addresses, and phone numbers of public health organizations providing information/materials/programs for smoking cessation
Requirements concerning signs and labels
29 CFR 1926.1101(k)

## Slide 91: Employee Information and Training Class I and Class II
Class I Jobs
  Equivalent to EPA MAP asbestos abatement worker training
Class II Work
  Must include “hands-on” training and specific work practices and engineering controls for the category of materials as well as basic information required for all employees
Class II Work
  With asbestos-containing roofing materials, flooring materials, siding materials, ceiling tiles, or transite panels must be at least 8 hours
29 CFR 1926.1101(k)

## Slide 92: Employee Information and Training Class III
Consistent with the EPA training course for local education agency maintenance and custodial workers who will disturb ACM or PACM (40 CFR 763.92(a)(2))
Must include “hands-on” training and take at least 16 hours
Exception: If a competent person determines the EPA curriculum is not adequate, training must include the basic information as well as specific applicable work practices and controls and “hands-on “ training
29 CFR 1926.1101(k)

## Slide 93: Employee Information and Training Class IV
Consistent with EPA requirements for training local education agency maintenance and custodial workers who contact but do not disturb ACM or PACM
At least 2 hours
Include:
  Location of ACM/PACM, asbestos-containing flooring material, or flooring material where absence of asbestos has not been certified
  Instruction in recognition of damage, deterioration, and delamination of asbestos-containing building materials
29 CFR 1926.1101(k)
Notes: (40 CFR 763.92(a)(1))

## Slide 94: Employee Information and Training Access
Make available to employees without cost
  Written materials relating to training program
  Copy of the Standard
  NIH Publication No. 89-1647 or equivalent self-help smoking cessation program material
Provide to OSHA and NIOSH upon request all information and training materials
29 CFR 1926.1101(k)

## Slide 95: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101(l)

## Slide 96
Notes: Now let’s discuss the housekeeping requirements of this standard

## Slide 97: Housekeeping
Vacuuming
  HEPA-filtered equipment
  Used and emptied so minimizes reentry of asbestos into workplace
Asbestos waste and contaminated articles consigned for disposal
  Collected and disposed of in sealed, labeled, impermeable bags or other containers
Dust and debris in areas containing accessible TSI or surfacing ACM/PACM or visibly deteriorated ACM
  No dry sweeping or vacuuming without HEPA filters
  Prompt cleanup and disposal in leak-tight containers
29 CFR 1926.1101(l)

## Slide 98: Housekeeping
Care of asbestos-containing flooring material
  No sanding
  Strip finish only with low abrasion pads, speed < 300 rpm, and wet methods
  Burning or dry buffing only on flooring with sufficient finish so pad cannot contact flooring material
29 CFR 1926.1101(l)

## Slide 99: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101(m)

## Slide 100
29 CFR 1926.1101(m)
Notes: Medical surveillance under paragraph (m)

## Slide 101: Medical Surveillance Employees Covered
Class I, II and III work for a combined total of 30 or more days/year
Exposed ≥ PELs for total of 30 days/year
  Days of Class II or III work where the work is 1 hour or less and other work practices are required by the standard are complied with, do not count in the total Employees
Otherwise required to wear negative pressure respirators by this standard must have this use approved by a physician
29 CFR 1926.1101(m)(1)

## Slide 102: Medical Surveillance Examination
By or under the supervision of a licensed physician
No cost to the employee
Reasonable time and place
PFTs administered by:
  Licensed physician or
  Person who has completed a training course in spirometry sponsored by an appropriate academic or professional institution
29 CFR 1926.1101(m)(1)
Notes: PFTs = pulmonary function tests

## Slide 103: Medical Surveillance Examinations and Consultations
Prior to assignment to an area where negative-pressure respirators are worn
Within 10 working days of the 30th day of exposure, within one year, for employees
  Engaged in Class I, II, and/or III work
Annually thereafter
More frequently when recommended by the physician
Exception:
  No examination required if examined within past 1-year period
29 CFR 1926.1101(m)(1)

## Slide 104: Medical Surveillance Content
Medical and work history (special emphasis to pulmonary, cardiovascular, and gastrointestinal systems
Standardized questionnaires
  Initial examination: Appendix D, Part 1
  Annual examinations: Appendix D, Part 2
Physical examination directed to pulmonary and gastrointestinal systems
  Chest X-ray (physician’s discretion)
  Pulmonary
    FVC
    FEV(1)
  Other examinations/tests as ordered by physician
29 CFR 1926.1101(m)(1)
Notes: c/v = cardiovascular
g/I = gastrointestinal

## Slide 105: Medical Surveillance Information Provided to Physician
Copy of the standard and Appendices D, E, and I
Description of employee’s duties relative to exposure
Representative exposure level or anticipated exposure level
Description of PPE and respirators used
Information from previous medical examinations
29 CFR 1926.1101(m)(1)

## Slide 106: Medical Surveillance Physician’s Written Opinion
Content
  Results of medical examination
  Whether employee has any medical conditions that would increase risk of impairment from exposure to asbestos
  Recommended limitations on employee or on use of PPE (e.g., respirators)
  Statement that physician has informed employee of exam results and of any medical conditions that may result from asbestos exposure
  Statement that employee has been informed of increased risk of lung cancer due to smoking and asbestos exposure
29 CFR 1926.1101(m)(1)

## Slide 107: Medical Surveillance Physician’s Written Opinion
May not include findings or diagnoses unrelated to occupational exposure to asbestos
Must be provided by employer to employee within 30 days of receipt
29 CFR 1926.1101(m)(1)

## Slide 108: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101(n)

## Slide 109: Recordkeeping Exposure Measurements
Record must include:
  Date of measurement
  Operation being monitored
  Sampling and analytical methods used and
  evidence of their accuracy
  Number, duration, and results of samples
  Type of protective devices worn
  Name, social security number, and exposure of employees whose exposures are represented
Record must be maintained for at least 30 years
Employer may have records maintained by industry trade and employee associations
29 CFR 1926.1101(n)

## Slide 110: Recordkeeping Objective Data
Record must include:
  Product qualifying for exemption
  Source of the objective data
  Testing protocol, results of testing, and/or analysis of material for the release of asbestos
  Description of operation exempted and how data support exemption
  Other data relevant to operations, materials, processing, or employee exposures covered by exemption
Record must be maintained for duration of reliance upon the objective data
29 CFR 1926.1101(n)

## Slide 111: Recordkeeping Medical Surveillance
Record must include:
  Employee’s name and SSN
  Copy of employee’s medical exam results
  Physician’s written opinions
  Employee medical complaints related to exposure to asbestos
  Copy of information provided to physician
Maintained for employment + 30 years
29 CFR 1926.1101(n)
Exam Results

## Slide 112: Recordkeeping Other Records
Training records
  Must be maintained for 1 year beyond last date of employment by that employer
Data to rebut PACM
  Kept for duration used to rebut presumption
Records of required notifications
  Must be maintained by building owner for duration of ownership and must be transferred to successive owners
29 CFR 1926.1101(n)

## Slide 113: Recordkeeping Records Availability and Transfer
Upon written request, all records are available to OSHA and NIOSH for examination and copying
Upon request, exposure records are available to employees, former employees, designated representatives, and OSHA for examination and copying
Upon request, employee medical records are available to the subject employee, anyone having the employee’s written consent, and OSHA for examination and copying
29 CFR 1910.1020(h) governs transfer of records
When an employer ceases business without a successor employer, the employer must notify NIOSH 90 days before disposal of records and transmit them to NIOSH if requested
29 CFR 1926.1101(n)

## Slide 114: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101(o)

## Slide 115: Competent Person General
“On all construction worksites covered by this standard, the employer shall designate a competent person, having the qualifications and authorities for ensuring worker safety and health required by Subpart C, General Safety and Health Provisions for Construction (29 CFR 1926.20 through 1926.32).”
29 CFR 1926.1101(o)

## Slide 116: Competent Person Frequency of Inspections
Required inspections - frequent and regular inspections of job sites, materials, and equipment
Additional inspections
  Class I jobs
    At least once during each work shift
    At any time at employee request
  Class II, III, and IV jobs
    At intervals sufficient to assess whether
    conditions have changed
    At any reasonable time at employee
    request
29 CFR 1926.1101(o)

## Slide 117: Competent Person Duties
Class I or II jobs, perform or supervise
  Set up of regulated area, enclosure, or other containment
  Ensuring integrity of enclosure or containment
  Set up of procedures to control entry to and exit from the enclosure and/or area
  Supervision of employee exposure monitoring
  Ensuring that employees working within enclosure
  and/or using glove bags wear required protective
  clothing and respirators
29 CFR 1926.1101(o)

## Slide 118: Competent Person Duties
Ensure employees set up remove/engineering controls, and use work practices and PPE as required
Ensure employees use hygiene facilities and decontamination procedures as required
Ensure engineering controls are functioning properly and employees are using proper work practices
Ensure notification requirements are met
29 CFR 1926.1101(o)

## Slide 119: Competent Person Training Class I and II
Comprehensive course for supervisors meeting criteria of EPA MAP (40 CFR 763, subpart E, Appendix C) for stringency, content, and length
Contents - all aspects of asbestos removal and handling
  Abatement, installation, removal, and handling
  Contents of the standard
  Identification of asbestos
  Removal procedures
  Other practices for reducing the hazard
29 CFR 1926.1101(o)

## Slide 120: Competent Person Training Class III and IV
Contents - aspects of asbestos handling appropriate to the work
  Procedures for setting up glove bags and mini-enclosures
  Practices for reducing asbestos exposures
  Use of wet methods
  Contents of the standard
  Identification of asbestos
Equivalent in stringency, content, and length to EPA requirements for training local education agency maintenance and custodial workers (40 CFR 763.92(a)(2))
29 CFR 1926.1101(o)

## Slide 121: Asbestos in Construction
  Scope and application
  Definitions
  Permissible exposure limits
  Multi-employer worksites
  Regulated areas
  Exposure assessments and monitoring
  Methods of compliance
  Respiratory protection
Protective clothing
Hygiene facilities
Communication
Housekeeping
Medical surveillance
Recordkeeping
Competent person
Appendices
29 CFR 1926.1101(p)

## Slide 122: Appendices
Mandatory
A - OSHA Reference Method
C - Qualitative and Quantitative Fit Testing Procedures
D - Medical Questionnaires
E - Interpretation and Classification of Chest Roentgenograms
Non-Mandatory
B - Sampling and Analysis
F - Work Practices and Engineering Controls for Class I Asbestos
Operations
H - Substance Technical Information for Asbestos
I - Medical Surveillance Guidelines for Asbestos
J - Smoking Cessation Program Information for Asbestos
K - Polarized Light Microscopy of Asbestos
Reserved
G
29 CFR 1926.1101(p)

## Slide 123: Asbestos in General Industry
  Scope and application
  Definitions
  Permissible exposure limits
  Exposure monitoring
  Regulated areas
  Methods of compliance
  Respiratory protection
  Protective work clothing and equipment
Hygiene facilities and practices
Communication of hazards
Housekeeping
Medical surveillance
Recordkeeping
Observations of monitoring
Dates
Appendices
29 CFR 1910.1001

## Slide 124: Methods of Compliance Engineering and Work Practice Controls
Implemented to reduce < PEL
Particular operations
  Coupling cut-off in 1° asbestos cement pipe mfg.
  Sanding in 1° and 2° asbestos cement sheet mfg.
  Grinding in 1° and 2° friction product mfg.
  Carding and spinning in dry textile products
  Grinding and sanding in 1° plastics mfg.
Notes: When eng. ctls. & work practices not sufficient to bring below PELs, must implement to bring to or below 0.5 f/cc or 2.5 f/cc (EL) and supplement w/ respirators

## Slide 125: Methods of Compliance Particular Tools
All hand-operated and power-operated tools which would produce or release fibers of asbestos equipped with LEV
Examples:
  Saws
  Scorers
  Abrasive wheels
  Drills

## Slide 126: Methods of Compliance Engineering and Work Practice Controls
Wet methods
Particular products and operations
Compressed air
Flooring
Written compliance plan
Brake and clutch repair
Notes: Wet methods of handling, mixing, applying, removing, cutting or scoring of asbestos material.
Particular products & operations: No asbestos cement, mortar, coating, grout, plaster, or similar material containing asbestos, shall be removed from bags, cartons, or other containers in which they are shipped, without being either wetted, or enclosed, or ventilated so as to prevent effectively the release of airborne fibers.
Compressed air cannot be used w/o point of capture LEV
Sanding of ACM flooring prohibited
Specific work practices for asbestos brake and clutch repair

## Slide 127: Communication of Hazards
Installed ACM (< 1980)
  Examples:
    TSI, SM
    Asphalt/vinyl flooring
Employers
Building and facility owners
Warning labels
Notes: Warning signs must be posted at entrance to mechanical rooms/areas where ACM or PACM present

## Slide 128: Communication of Hazards
Warning signs
MSDS
Employee information and training
  Initial
  Annual
Criteria to rebut PACM
Notes: Warning signs must be posted at entrance to mechanical rooms/areas where ACM or PACM present

## Slide 129: Housekeeping
Care and maintenance of asbestos flooring
  Sanding of ACM flooring prohibited
  Stripping of finishes
    Low abrasion pads
    < 300 rpm
    Wet methods
  Burnishing or dry buffing only on
  floors with sufficient finish

## Slide 130: Medical Surveillance
Pre-placement examination
Periodic (annual) examination
Termination of employment examination
Notes: Termination exam if exposed at or above TWA and/or EL

## Slide 131: Recordkeeping
Exposure measurements
  30 yrs
Objective data
  Period of reliance
Medical surveillance
  Employment + 30 yrs
Training records
  1 yr beyond last employment date

## Slide 132: Appendices
A, D, E and F – Mandatory
B, G, H, I and J – Informational

## Slide 133: Thank You For Attending!
Final Questions?
1-800-NC-LABOR
(1-800-625-2267)
www.nclabor.com