## Slide 1: N.C. Department of Labor OSH Division
Laboratory Safety and Health
29 CFR 1910.1450
Notes: Rev 0: 6/24/2013

## Slide 2: Frankenstein’s Lab, SIC 8731…
Notes: I also want to add that:
I am not a chemist
I am not a lab expert
I do not know it all, BUT
I love to learn and it is my hope that I can teach you something and that you can teach me something.
I have 2 hours to cover this material, and most of you in here will have heard much of this before. I don’t want this to be a lecture in industrial hygiene/chemistry, nor do I want to ignore it for the sake of those in this class that do not have that knowledge by way of education or experience. I want everyone to get something from this class. I can tell you honestly that putting this presentation together has been a great review for myself!

## Slide 3: Course Objectives
Provide overview of the “Occupational exposure to hazardous chemicals in laboratories” (a.k.a. “The Lab Standard”)
Enable CSHO to correctly cite lab standard by:
  Defining laboratory use
  Identifying the types of laboratories covered by the standard
  Identifying exceptions (when to cite the other health standards in Subpart Z or the lab standard)
Know what to look for in a lab by understanding the employer’s Chemical Hygiene Plan.
Identify other “shall’s” of the lab standard
29 CFR 1910.1450
Notes: A few of the pictures, stories, slides are taken from the OSHA TI Course in Salt Lake City Utah.
The course lasted for 3.5 days, and one day was spent at the Salt Lake Technical Center where Federal OSHA and some state plan states sent their field samples (air, soil, bulk, etc.) to be analyzed.
The class walked through the laboratory to evaluate it for safety and health hazards (for violations of the lab standard and other applicable standards).
We were also provided a copy of their Chemical Hygiene Plan.
The first few days of the class we covered the lab standard, chemical hazards, flammables, compressed gases, emergency response, and bio-safety.
I learned a lot just from the first day of class when we covered the scope and application of the lab standard. The scope is vital to the correct application of this standard. There are many compliance officers that incorrectly cite the lab standard, based solely on the scope.
Other aspects of the OSHA TI course on lab safety that was beneficial was
The class participation (hint, hint)…there were a variety of questions representing the many different backgrounds in the classroom. There were compliance officers, consultants, and people from private industry. Many state plan states were represented as well.
2. The presenter (chair person, Jim Miller) was very professional, and knowledgeable in the subject manner.
The field trip to the SLTC was interesting (getting to see where/how samples are analyzed), and getting to apply some of what we learned in class.
4. It was good to hear stories, pictures, accidents, and fatalities from various locations throughout the country.
The OSHA TI course really taught me a lot about the lab standard, but I am finding that Laboratory Safety and Health goes well beyond the standard.
For this presentation, I have borrowed information and pictures from Duke (where I worked before coming to OSHA), from the HazMat team (RRT-4) for which I am a member of, from the internet, NCOSH intranet, and Fed OSHA website, from the course information presented in Utah, and a little from my job at East Carolina School of Medicine as a Radiation Safety Technician, and many other resources. I have also referred to several Chemical Hygiene Plans from different companies.
I will cover every paragraph of the Lab Standard, spending time on the more pertinent parts of it.
I will cover other safety and health items/issues that may be encountered in the laboratory, but covered by a different standard. This may help you answer the question “what am I looking for in here?”
There are Appendices attached to your presentation package including a glove selection guide and resources, chemical incompatibility charts, example inspection checklist, and an expanded health standard chart.
If there is time, I have a really good 30 minute video that may help put some of this information into perspective.

## Slide 4: Objective 1 Correctly Cite the Lab Standard
Scope and application
  This section shall apply to all employers engaged in the laboratory use of hazardous chemicals.
29 CFR 1910.1450(a)(1)

## Slide 5: Scope and Application
Exceptions to citing the lab standard
Supersedes all OSHA health standards in 29CFR 1910, Subpart Z, except:
  Employee exposure shall not exceed PEL’s already set by other standards
  Prohibition of skin and eye contact set by other standards shall be observed
  Where an action level is routinely exceeded for an OSHA regulated substance, the exposure monitoring and medical surveillance requirements paragraphs (d) and (g)(1)(ii) of this section shall apply.
29 CFR 1910.1450(a)
Notes: Where this section applies, it shall supersede, for laboratories, the requirements of all other OSHA health standards in 29 CFR part 1910, subpart Z, except as follows:1910.1450(a)(2)(i) For any OSHA health standard, only the requirement to limit employee exposure to the specific permissible exposure limit shall apply for laboratories, unless that particular standard states otherwise or unless the conditions of paragraph (a)(2)(iii) of this section apply.1910.1450(a)(2)(ii) Prohibition of eye and skin contact where specified by any OSHA health standard shall be observed.1910.1450(a)(2)(iii) Where the action level (or in the absence of an action level, the permissible exposure limit) is routinely exceeded for an OSHA regulated substance with exposure monitoring and medical surveillance requirements paragraphs (d) and (g)(1)(ii) of this section shall apply.
MS Clip Art

## Slide 6: Scope and Application
Does not apply to:
  Use of hazardous chemicals which do not meet the definition of laboratory use
  Lab use of hazardous chemicals having no potential for exposure, such as:
    Chemically-impregnated test media
    Commercially prepared kits such as those used to perform pregnancy testing
29 CFR 1910.1450(a)
Notes: 1910.1450(a)(3) This section shall not apply to:1910.1450(a)(3)(i) Uses of hazardous chemicals which do not meet the definition of laboratory use, and in such cases, the employer shall comply with the relevant standard in 29 CFR part 1910, subpart Z, even if such use occurs in a laboratory.1910.1450(a)(3)(ii) Laboratory uses of hazardous chemicals which provide no potential for employee exposure. Examples of such conditions might include:1910.1450(a)(3)(ii)(A) Procedures using chemically-impregnated test media such as Dip-and-Read tests where a reagent strip is dipped into the specimen to be tested and the results are interpreted by comparing the color reaction to a color chart supplied by the manufacturer of the test strip; and1910.1450(a)(3)(ii)(B) Commercially prepared kits such as those used in performing pregnancy tests in which all of the reagents needed to conduct the test are contained in the kit.
MS Clip Art

## Slide 7: Definitions
Laboratory use
  Handling or use of such chemicals in which ALL the following conditions are met:
    Chemical manipulations are carried out on a “laboratory scale”
    Multiple chemical procedures or chemicals are used
    The procedures involved are NOT part of a production process
    “Protective laboratory practices and equipment” are available and in common use
29 CFR 1910.1450(b)
Notes: Chemical manipulations simply means the use of chemicals.
3.Production simply means operation where a product is produced such as, refineries, utility-generating companies, manufacturing plants.
4.”Protective laboratory practices and equipment” means those laboratory procedures, practices and equipment accepted by laboratory health and safety experts as effective, or that the employer can show to be effective, in minimizing the potential for employee exposure to hazardous chemicals. ***The intent refers that a body of information, accepted by safety and health experts is AVAILABLE. Not to exclude those labs from coverage if they did not have these practices and equipment.
  Private sector QC labs are not covered: (“I’m doing it to prove my product is okay”)… Testing incoming product and outgoing product. These labs will fall under HazCom. If they do ANYTHING else, then they are covered. **QC exemption only for private sector manufacturing a product. Quality Control Labs generally not covered because they are usually adjuncts of production operations.
  Municipalities – potable water – production is QC OR electrical power generation water treatment labs.
  Photography labs are QC
  Dental Labs are production/QC
  Production pharmacies are QC
  No and Yes to Small Medical Labs drawing blood (No if just drawing blood and no other activities are involved—biohazards are not w/in the scope. YES if use chemicals to analyze the blood.
YES: Any EPA compliance work (testing wastewater effluent, air quality, etc.) simply for determining compliance with EPA discharge criteria is covered . This would only be considered QC if the results of the monitoring are used as a source of info. for process control adjustment.
Yes to I.H. labs doing asbestos analysis all day long.
Yes to bench scale operations that look @ substitutes for processes. (It is considered research).
Yes/No to soil & water analysis of unknowns (yes, so long as not assuring product liability).
Yes/No to Labs that use toxic materials just for calibration (Yes, if calibration is for purposes other that QC, AND assuming ee’s are exposed to toxic materials.)
SIC codes are not used as a criteria for scope of coverage.
Repetitive nature is not criteria used in determining coverage. This was mentioned in the preamble as one of the characteristics that labs generally have.

## Slide 8: Definitions
Laboratory scale
  Containers used for reactions, transfers, and other handling of substances are designed to be easily and safely manipulated by one person.
(Excludes those workplaces whose function is to produce commercial quantities of materials.)
29 CFR 1910.1450(b)
Notes: Mention PSM
OSHA developed definitions for “laboratory scale” and “laboratory use” so as to focus on the CONDITIONS of the workplace rather than on the word “laboratory” itself.
Quantity limits is not a criteria for laboratory scale. So, instead it is defined in relation to the size of containers

## Slide 9: Definitions
Laboratory
  A facility where the “laboratory use of hazardous chemicals” occurs.
  It is a workplace where relatively small quantities of hazardous chemicals are used on a non-production basis.
29 CFR 1910.1450(b)
Notes: Laboratory as defined is not subject to the PSM stds (“relatively small quantities” is less than the threshold quantities of hazardous chemicals listed in the PSM std.)

## Slide 10: Definitions
Chemical hygiene officer
  Employee designated by employer that has the training or experience to provide technical guidance in the development and implementation of the Chemical Hygiene Plan.
    Definition not intended to place
    limitations on the position description
    or job classification that the designated
    individual holds within the employer's
    organizational structure.
29 CFR 1910.1450(b)
Notes: Chemical Hygiene Officer means an employee who is designated by the employer, and who is qualified by training or experience, to provide technical guidance in the development and implementation of the provisions of the Chemical Hygiene Plan. This definition is not intended to place limitations on the position description or job classification that the designated individual shall hold within the employer's organizational structure.
MS Clip Art

## Slide 11: Definitions
Chemical hygiene plan
  Written program developed and implemented that sets forth procedures, equipment, personal protective equipment and work practices that protect employees from health hazards presented by hazardous chemicals used in the workplace
29 CFR 1910.1450(b)
Notes: Chemical Hygiene Plan means a written program developed and implemented by the employer which sets forth procedures, equipment, personal protective equipment and work practices that (i) are capable of protecting employees from the health hazards presented by hazardous chemicals used in that particular workplace and (ii) meets the requirements of paragraph (e) of this section.
MS Clip Art

## Slide 12: Definitions
Hazardous chemical
  Chemical that has statistically significant evidence that acute or chronic health effects may occur in exposed employees.
  “Health hazard" includes carcinogens, toxic agents, reproductive toxins, irritants, corrosives, sensitizers, hepatotoxins, nephrotoxins, neurotoxins, agents which act on the
  hematopoietic systems, those that damage
  the lungs, skin, eyes, or mucous membranes.
29 CFR 1910.1450(b)
Notes: Hazardous chemical means a chemical for which there is statistically significant evidence based on at least one study conducted in accordance with established scientific principles that acute or chronic health effects may occur in exposed employees. The term "health hazard" includes chemicals which are carcinogens, toxic or highly toxic agents, reproductive toxins, irritants, corrosives, sensitizers, hepatotoxins, nephrotoxins, neurotoxins, agents which act on the hematopoietic systems, and agents which damage the lungs, skin, eyes, or mucous membranes. Appendices A and B of the Hazard Communication Standard (29 CFR 1910.1200) provide further guidance in defining the scope of health hazards and determining whether or not a chemical is to be considered hazardous for purposes of this standard.
MS Clip Art

## Slide 13: When are employees covered?
At least one employee doing analysis
Laboratory use
At least one chemical
Must be a potential for employee exposure
  Examples of conditions of no exposure
    Dip and read tests
    Commercially prepared kits
Notes: All employers engaged in the laboratory use of hazardous chemicals.
Define laboratory use: on next slide
(2)
Can be any employee, any where **There is no size requirements (can be 1 person in a mobile unit, tent, etc.) **ALSO, maintenance and custodial may be included. But not visitors or sales people.
There has to be at least ONE Chemical (no physical testing labs)
  Chemicals ONLY– does not apply to biohazard (go general duty or bloodborne standard) until extracted and manipulated.
Ex. Dog bite with rabies = biohazard
But if you extract the rabies and research on = chemical
All human samples (blood, etc.) will apply because using other chemicals to research it.
No potential for employee exposure examples:
    Procedures using chemically-impregnated test media such as Dip-and-read tests where a reagent strip is dipped into the specimen to be tested and the results are interpreted by comparing the color reaction to a color chart supplied by the manufacturer of the test strip.
        Ex. The tests used at the doctors office for checking urine for level of glucose, protein, etc.
    Commercially prepared kits in which all of the reagents needed to conduct the test are contained in the kit.
        Ex. pregnancy test
    Automated tests

## Slide 14: The Formaldehyde Exception
The use of formaldehyde in histology, pathology and anatomy labs will remain under the formaldehyde standard, as directed by that standard.
All other uses of formaldehyde will be covered by the lab standard.
  Found in the Federal Register, Vol. 55, No. 21 Supplementary Information, Summary of Issues and Explanations of Provisions of the Final Standard, Paragraph (a) Scope and Application, Preemption by Other OSHA Health Standards.

## Slide 15: Does the lab standard apply?
Wastewater Lab
Yes
QC Lab
No
Notes: EPA discharge criteria!
QC is usually an adjunct of a production process

## Slide 16: Does the lab standard apply?
R & D
Yes
Physical Testing Lab
No
Notes: Mount Olive Pickle
Remember, there must be at least one chemical!

## Slide 17: Does the lab standard apply?
Computer Lab
No
NASA Bio-Technology Lab
Yes
Notes: Ha Ha
Biotechnology is an upcoming thing in the world with the space station. It would be great work as an IH

## Slide 18: Does the lab standard apply?
Physical Testing Lab
No
Clandestine Lab
Yes
Notes: Clandestine labs are illicit operations consisting of chemicals and equipment necessary to manufacture controlled substances. They can be in mountain cabins, rural farms, single and multifamily residences, in urban and suburban neighborhoods.
Drugs like methamphetamine, PCP, MDMA, methcathinone, require little knowledge or equipment. LSD requires much higher levels of expertise.

## Slide 19: Does the lab standard apply?
Medical Research
Yes
Clandestine Methamphetamine Lab
Yes
Notes: Research, so long as all conditions are met. Lab std does not apply to biologicals or radiologicals

## Slide 20: Does the lab standard apply?
Physician’s Clinic Lab
No? Maybe Yes
Water Treatment Labs
No
Notes: No, and yes, really depends on what is being done. If just drawing blood and no other activities are performed then no (as biohazards are not within the scope). If used chemicals to analyze blood, then yes it is covered.
Water treatment is production (water is the product). And may be analyzing the water for quality control purposes.

## Slide 21: Does the lab standard apply?
NC Regional Response HazMat Team 4 (RRT 4)
Yes!
Notes: Yes. Research. Mobile unit. Analyzing unknowns

## Slide 22: Does the lab standard apply?
Notes: Do we need a chemical hygiene plan???
Remember: Failure to fit within the scope and application section of the lab std. Merely shifts the employer’s obligation to compliance with the appropriate general industry standards. Moreover, it should be noted that the general duty clause, section 5 (a)(1) of the OSH Act, continues to be applicable to all employers

## Slide 23: PELs
For laboratory uses of OSHA regulated substances, the employer shall assure the employees’ exposures to such substances do not exceed the permissible exposure limits specified in 29 CFR 1910, Subpart Z.
29 CFR 1910.1450(c)

## Slide 24: Employee Exposure Determination
Initial monitoring
  Employer shall measure exposure for any chemical with a standard if there is reason to believe that exposure exceed, routinely, the action level or PEL
Periodic monitoring
  If the initial monitoring show exposure over the action level or PEL, the employer shall comply with monitoring requirements of the relevant standard
29 CFR 1910.1450(d)
Notes: First meet the definition of lab use (if doesn’t, then must comply with relevant std. even though it occurs in a lab.
Second, there must be a potential for employee exposure.
Keep in mind… Workers are often exposed to a mixture of hazardous substances which may produce a variety of toxic reactions. Such reactions may be synergistic or additive. Mixed exposures would be more common in labs than in general industry…(lab std. History)

## Slide 25: Employee Exposure Determination
Termination of monitoring
  Per the applicable standard
Employee notification of monitoring
  Within 15 working days of getting results, notify employees in writing individually or by posting in appropriate, accessible location
29 CFR 1910.1450(d)

## Slide 26: Objective 2 Chemical Hygiene Plan
29 CFR 1910.1450(e)
Notes: The chemical hygiene plan is the heart of the lab standard. It is the employer’s policy, procedure, approach to handling safety and health in a laboratory setting.
The plan shall:
1) Be capable of protecting employees from health hazards associated with hazardous chemicals and
2) Be capable of keeping exposures below the specific exposure limits specified in paragraph ( c) and as stated earlier.
The question as to whether a CHP would be required for each individual laboratory in establishments with many separate laboratory operations or whether a single facility-specific plan would suffice, should be decided locally by the facilities covered. Ideally, the plan should be specific enough to a particular workplace that it does not require employees to familiarize themselves with extraneous material that is not relevant.
(3) The plan shall include the following elements and shall indicate specific measures to ensure employee protection..
SOPs

## Slide 27: Chemical Hygiene Plan
The employer shall develop and carry out provisions of a plan where hazardous chemicals are used in the workplace to:
  Protect employees from health hazards, and
  Keep exposures below PELs
The Plan must be readily accessible to employees and others as defined
Please note: Non-mandatory Appendix A of the Lab Standard 1910.1450 provides guidance to assist employers in plan development.
29 CFR 1910.1450(e)(1)-(2)

## Slide 28: Chemical Hygiene Plan
The plan shall include the following elements and and shall indicate specific measures to ensure employee protection:
  Standard Operating Procedures (SOPs) , Safe Work Practices (SWPs), or Standard Operating Guidelines (SOGs)
    Developed to ensure employees are
    protected from all potentially hazardous
    chemicals in use in their work area
29 CFR 1910.1450(e)(3)(i)
Notes: The CHP must include necessary work practices, procedures, and policies to ensure employee’s are protected from all potentially hazardous chemicals in use in their work area.
Written safe work practices are often the most important component of a good safety program, esp. when used for training and education.

## Slide 29: NCSU’s Chemistry Department Chemical explosion
Notes: Reagent being prepared on the day of the incident was for a general chemistry lab titration that involved adding potassium permanganate powder to concentrated sulfuric acid. The reaction that took place resulted in an explosion. The chemical mixture splashed on the employee resulting in second and third degree burns.
The eyewash safety shower was 70+ feet from the lab and the path to get to it involved going through two doors and maneuvering around lab benches. Sometimes the lab with the eyewash/safety shower is closed and locked. Safety glasses and nitrile gloves were worn. No lab coat. No face shield. She had safety/haz com training (inc. MSDSs). The PPE required to be worn while working with conc. Acids was not provided by the employer. She had done this procedure several times but usually only made half the volume. The procedure was not in writing, but was shown to her by a previous lab technician.
Rule of thumb:
Never add anything to a concentrated acid unless the final solution is a conc. Acid. Dilute the acid first.
Oxidizers (such as KMnO4) are incompatible with strong acids
Check your MSDSs AND other chemistry resources.
“Do what you outta add acid to wata”
How/ What would you cite?

## Slide 30: SOP’s = Chemical Explosion
Notes: The splatter from the explosion reached the ceiling and all sides of the room.
Here you can see the melted trash can directly across from the fume hood where the explosion occurred.

## Slide 31: Chemical Explosion
Notes: In the absence of safe work practices, exposure to hazardous chemicals in the laboratory presents a significant risk of material health impairment (remember the discussion of significant risk?)

## Slide 32: How can the employer ensure safety and health through SOPs?
The employer must write in the SOP/SWP what the procedure is, how to perform the procedure (what materials are needed), what reagents are used, what reactions will take place, (all from a safety perspective)
  What PPE is required
  How to order the chemical
  How to store and dispose of the chemicals

## Slide 33: Chemical Hygiene Plan Control Measures
Criteria that will be used to determine and implement control measures to reduce employee exposure to hazardous chemicals including:
  Engineering controls
  PPE and hygiene practices
  Control measures for chemicals that are known to be extremely hazardous
29 CFR 1910.1450(e)(3)(ii)
Notes: We will talk about each of these as we move along through the presentation

## Slide 34
Criteria that will be used to determine and implement control measures to reduce employee exposure to hazardous chemicals including:
  Engineering controls
  PPE and hygiene practices
  Control measures for chemicals that are known to be extremely hazardous
Chemical Hygiene Plan Control Measures
29 CFR 1910.1450(e)(3)(ii)

## Slide 35: Examples of Engineering Controls
How often are fume hoods inspected?
Who certifies the hoods?
What if the hood doesn’t pass inspection?
Are there BSC’s (biological safety cabinets)?
Eyewash and safety shower inspections?
Fire extinguisher inspections?
Chemical stockrooms/ storerooms?
Ventilated storage cabinets?
Power failure controls?
What happens to the exhausted air from BSC’s, isolation rooms, stockrooms, etc?….

## Slide 36: Examples of Engineering Controls
Laboratory ventilation
  Facility’s heating and air conditioning system
  Fume hoods (are NOT biological safety cabinets!!)
Transport of chemicals
Flammable storage
Sharps use?
Notes: Laboratory ventilation is a key factor in controlling employee exposure to hazardous substances. Ventilation is provided in two ways:
Through the facility’s heating and air conditioning system
And through fume hoods utilized in the laboratory
* Fume hoods are not be used as a substitute for Biological Safety Cabinets (BSC) which are laminar flow hoods. Or vice versa.

## Slide 37: Engineering Controls Laboratory Ventilation
Types of laboratory hoods
  Enclosure hoods
    Exhaust hoods with HEPA filters (ex. For use with asbestos)
    Perchloric acid hoods
    Walk-in hoods
Capturing type hoods
  Slot vents
Flex ducts
Glove box
Notes: NIOSH was requested on several occasions to evaluate employee exposures to xylene, formaldehyde, chloroform, toluene, and methyl methacrylate in histology, cytology, and surgical pathology labs following employee complaints of respiratory and behavioral problems. The investigations did show in some instances, a health hazard did exist. Major contributors to the hazardous conditions included ineffective exhaust ventilation and poor work practices.
OSHA’s definition of a fume hood is a “device located in the laboratory which is enclosed on five sides with a movable sash or fixed particle enclosure on the remaining side; constructed and maintained to draw air from the laboratory and to prevent or minimize the escape of air contaminants into the lab; and allows chemical manipulations to be conducted in the enclosure without insertion of any portion of the employee’s body other than hands and arms.
Fume hoods are used for the safe handling of noxious, corrosive, or volatile chemicals. They reduce worker exposure to chemical vapors, gases, fumes and dusts generated in the laboratory and reduces the possibility of fire and explosion hazards inherent in chemical research and development.

## Slide 38: Engineering Controls Laboratory Ventilation
Bad Flow
Good Flow
Notes: When large obstructions are placed in the hood, the air flow is disrupted. This creates a dead air space in front of the obstruction and may create eddy currents sending chemical vapors out of the hood into the breathing zone of an employee.
Lowering the sash will increase the air velocity and offer greater protection from toxic fumes. Normally the sash opening should be less than 18”, and marked. This will help to keep the air flow within the minimum acceptable levels established for that hood.
Placing equipment no less than six inches in the hood will also reduce the possibility of fumes escaping into the laboratory.
Hoods should not be installed beside doors. The current from opening and closing doors can disturb the flow and create eddies.

## Slide 39: Engineering Controls Laboratory Ventilation
Perchloric acid hoods
  Constructed of stainless steel
  Have water rinse-down (wash-down) capabilities plumbed into them to remove perchloric acid or perchlorates from the duct work.
  Exhaust passes through a water-scrubber on the roof to remove acid vapors
Notes: Perchloric acid forms highly explosive and unstable compounds with many combustible materials and even with metals. Wood or asphalt tile on which perchloric acid has been spilled may spontaneously ignite.
Perchloric acid should be used with extreme caution and only in a fume hood specifically designed for this use.
Perchloric acid and sulfuric acid, when mixed, produce anhydrous perchloric acid which will ignite any organic material (like wood) and /or explode spontaneously.
All perchlorates should be considered as very explosive, especially on contact with organic materials. They are extremely shock sensitive.
Explosive crystals may form in perchloric acid bottles stored over long periods. For this reason, bottles should not be store for more than one year.

## Slide 40: Engineering Controls Transport of Chemicals
Move with a cart
Move without a cart
Notes: Moving compressed gas cylinders can be awkward (trust me, I know from experience in HazMat). There are several different types of carts designed to move different types/size cylinders.
Two people should move the liquid nitrogen dewars (they are very bulky and heavy).

## Slide 41: Engineering Controls Transport of Chemicals
Transport in hallways, etc.
Notes: Never transport open containers of chemicals through the hallways, stairs or in the elevator. All chemicals should be transported in rubber buckets, solvent jug carriers, pails, chemical transport carts (with special dividers to hold glass bottles), or some type of secondary containment device.
This is for containment of the chemical, should the original container be broken.

## Slide 42: Engineering Controls Flammable Storage
Notes: Flammable liquids should be stored in approved Safety Storage Cabinets.
They should never be stored with oxidizing agents, ex. Nitric, perchloric and sulfuric acids.

## Slide 43: Engineering Controls Flammable Storage
Notes: Safety cans should be used whenever possible, but should not be subjected to extreme changes in temperature or pressure.
Safety cans should have spring loaded caps with:
Pressure relief valve (allows the release of flammable vapors, which can accumulate—so beware);
A mechanism to prevent leakage or spillage if the can is dropped;
A mechanism to minimize vapor escape;
A flame arrestor to prevent fire from entering a safety can; and
“ “ to smother a fire inside the safety can.

## Slide 44
Wire mesh flame arrester
Flexible dispensing hose
Wire mesh flame arrester
Carrying handle is pulled back to open pouring valve and rear cap
Combination fill opening and relief vent
Engineering Controls Flammable Storage

## Slide 45: Engineering Controls Flammable Storage
Flammable/explosion proof refrigerators

## Slide 46: Engineering Controls Sharps Use
Notes: Various uses of sharps in labs…in analysis (GC’s and in liquid chromatography)…Think of or mention the use of CS2 (acts on central nervous system and has been implicated in some abortions).

## Slide 47
Criteria that will be used to determine and implement control measures to reduce employee exposure to hazardous chemicals including:
  Engineering controls
  PPE and hygiene practices
  Control measures for chemicals that are known to be extremely hazardous
29 CFR 1910.1450(e)(3)(ii)
Chemical Hygiene Plan Control Measures

## Slide 48: PPE and Hygiene Practices
What is the employer’s position on providing PPE at no cost?
What are the employer’s requirements for PPE?
  What PPE is required (eye protection, hand protection, etc.)?
  What type of PPE (goggles vs. face shield, nitrile vs. butyl gloves, etc.)?
  Where is it required?
  When is it required?
Contamination and laundering considerations

## Slide 49: PPE and Hygiene Practices
PPE
  Hand protection
  Eye/face protection
  Skin protection
  Foot protection
Hygiene
  Wash hands
  Never eat, drink, … in lab

## Slide 50: Why we need the right glove…
Dartmouth Researcher
Karen Wetterhahn
1948-1997
Notes: Skin contact is a very common route of chemical exposure. Usually, skin contact with chemicals will cause only local irritation or damage. Occasionally, however, skin contact with a chemical can be deadly.
Karen Wetterhahn, professor of chemistry at Dartmouth University, died at the age of 48 in 1997 from exposure to dimethylmercury. She had worked with this organo-metallic compound for years. However, she was wearing gloves that were not resistant to the chemical. One day, while preparing the mercury NMR standard, she spilled “one to several drops” of the dimethylmercury on the back of her gloved hand. The compound permeated the latex gloves she was wearing and was absorbed through her skin into the bloodstream. She said she had removed the glove promptly and did not think any more about the incident, and as a result, no medical monitoring or other follow-up was done. Mercury attacks the central nervous system well before the victim shows symptoms. It wasn’t until five months later that she began losing her balance and having trouble speaking. Tests showed that she had 80 times the lethal dose of mercury in her blood. Despite aggressive chelation treatment, Karen Wetterhahn went into a coma and died 10 months after exposure.
She was wearing disposable latex gloves.
Dimethylmercury is a rare compound, which can pass quickly through latex gloves, and usually without damaging them. It looks like water, but is three times as dense. The compound is attracted to the oil in human skin and is readily absorbed by the body.
Subsequent tests show that this compound permeates latex, PVC, and neoprene almost instantaneously (dimethylmercury migrates through plastics and rubber).
Lessons learned:
SOP’s
PPE selection
Hygiene practices
Training in hazards (inc. MSDS **but remember MSDS may not provide adequate guidance on glove selection)
Emergency Procedures/Equipment/spill response (cmpd has high vapor pressure)
Medical exams/consultation/surveillance
Selection criteria for chemicals with a high degree of acute toxicity, substitution?
“This tragedy highlights the need for research laboratories to develop a protective chemical hygiene plan which includes adequate guidance on the appropriate selection of PPE and engineering controls.
**Highly placed or very well qualified researchers should not be assumed to have adequate health and safety information. Research facilities should recognize that the nature of their work leads to diverse and often severe health hazards, and occupational health and safety must be proportionately pro-active.” -- The directorate of technical support.

## Slide 51: PPE Hand Protection
What material is best in glove selection?
  Low permeation rate
  High breakthrough time
The amount of a chemical
(steady state flow or
highest flow) which is
passed through a
given area of glove
material per unit time
(mg/m2/sec)
The elapsed time from
initial contact of the
chemical to the outside of
the glove to the first
detection of the chemical
on the inside glove
surface
Notes: Our hands are the body parts most likely to be exposed to chemical contact under normal situations. Even though careful technique may help an employee avoid direct contact with a chemical; the potential for exposure still demands the use of protective gloves.
1. There is no such thing as an impermeable glove. All chemicals will permeate through all glove materials. Gloves are considered protective if the permeation rate is slow enough that the chemical does not break through to the inside.
The objective in choosing a glove should be to seek a low permeation rate and a high breakthrough time, keep in mind:

## Slide 52: PPE Hand Protection
Keep in mind…
  Temperature need greater protection
  Double glove = quadruple duration of protection
  Solubility of chemical in the glove material
Remember…
  No “impermeable glove”
  No one glove material works for all
  chemicals
  For certain chemicals, no glove available
  which will provide > 1 hour protection
Notes: Permeation rates increase and breakthrough times decrease with increasing temperatures. You need greater protection if your chemical processes involve heat.
Thickness – Permeation is inversely proportional to thickness. Breakthrough time is directly proportional to the square of the thickness. Double gloving can quadruple the duration of protection.
Solubility – Permeation is a direct function of the solubility of the chemical in the glove material.

## Slide 53: PPE Hand Protection
What other factors are important?
  Resistance to physical damage
  Flexibility
  Heat resistance
  Incompatibilities
Notes: Many other factors must be considered when selecting the glove that best suits the task. Some of these factors include:
Resistance to Physical Damage—Do you need a glove that resists abrasions, cuts, punctures, or tears? A torn glove made of the perfect material is less protective than an intact glove made of another reasonably adequate material.
Flexibility – Is the ability to feel or manipulate small objects important or can you use a thicker more protective glove? Ex. HazMat and Firefighting
Heat Resistance – Do you have a hot operation? As stated in the previous slide, heat increases permeation rates. In addition, heat can lead to the breakdown of the glove material.

## Slide 54: PPE Hand Protection
Resources for glove selection
  Glove manufacturer
  MSDS’s
  “Prudent Practices in the Laboratory”
Web sites
www.bestglove.com
www.superiorglove.com/product.review/index.htm
http://www.ansellpro.com/specware/index.asp
Notes: The intent of have so much discussion of hand protection is because of it’s importance for life and wellness, and
to present an overview of the complex nature of selecting the correct glove for adequate protection.
Users should consult their Chemical Hygiene Officer and/or Safety Officer, their Standard Operating Procedures or Safe Work Practices, the MSDS, glove manufacturer’s literature and various other resources list here. Also I have attached an appendix which contains additional guidance on glove selection for specific chemicals.

## Slide 55: PPE Eye and Face Protection
Various types of eye protection in order of increasing effectiveness:
  Ordinary spectacles
  Safety glasses with side shields
  Protective goggles
  Face shields
  Head shields, which protect all of the head and throat
What is the company’s policy on
contact lenses?
Notes: Where there is potential of a corrosive chemical being splashed into the eyes, safety glasses or goggles AND a face shield should be worn. In situations where there is potential for an explosion to occur, head shields are required to safety glasses or goggles.
What is the company’s policy on Contact lenses?

## Slide 56: PPE Skin Protection
Notes: Lab coats should be worn when working with chemicals. Buttons and closures shall be used.
Always wear clothing that minimizes the amount of skin that can be exposed to potentially harmful chemicals. Never wear shorts in the lab.
??Wear an apron when working with acids or bases.

## Slide 57: PPE Foot Protection
Notes: No bare feet,
Shoe must cover top of foot, toe and heel
No pumps (doesn’t cover top of foot, slippery, and trip hazard b/c of high heel)
Cowboy boots are good because most likely leather, but may have a heel that is unacceptable.
Sneakers may be adequate (depending on whether canvas is appropriate or not).
Yes to a shoe that completely covers the foot, toe, and heel, flat sole, rubber sole? Leather shoe?

## Slide 58: Hygiene Practices
Notes: Wash hands often –
always before eating, smoking, drinking, applying cosmetics, and handling contact lenses
AND before leaving the laboratory…refer to accident described by Jim Miller in Utah about the man working with a chemical, wore gloves, handled a pen to take notes, intercom announces he has a phone call, he takes off gloves, answers the phone, takes the message using same pen, figures gloves are off he might as well go use the bathroom. Goes to the restroom, we are taught to wash hands afterwards, and he did.. But that didn’t help the subsequent burning of his leg and penis.

## Slide 59: Hygiene Practices
Ingestion
Contamination
Notes: Ingestion of chemicals occurs mostly through carelessness in the workplace. This might happen if a person puts their lunch or drink in a chemical refrigerator and someone spills a chemical on it.
Do not put objects (pencils, fingers, swabs, etc. in your mouth, ears or nose)

## Slide 60
Criteria that will be used to determine and implement control measures to reduce employee exposure to hazardous chemicals including:
  Engineering controls,
  PPE and hygiene practices,
  Control measures for chemicals that are known to be extremely hazardous
Chemical Hygiene Plan Control Measures
29 CFR 1910.1450(e)(3)(ii)

## Slide 61: Extremely Hazardous Chemicals
What is an extremely hazardous chemical?
  Resources for finding what is an extremely hazardous chemical:
    ACGIH TLVs, NIOSH, etc.
    Genium “Right to Know Pocket Guide for Laboratory Employees”
    Van Nostrand & Reinhold “ Condensed Chemical Dictionary”

## Slide 62: Extremely Hazardous Chemicals
What are the specific control measures in place for these chemicals?
  Chemical procurement
  Safe handling practices
  Description of PPE
  Air monitoring
  Emergency eyewash/shower facilities
  Working alone
Notes: Mention Johnston County Schools
Resources for finding what is a extremely hazardous chemical:
ACGIH, TLVs
Genium “Right to Know Pocket Guide for Laboratory Employees”
Van Nostrand & Reinhold “ Condensed Chemical Dictionary”

## Slide 63: Chemical Hygiene Plan Fume Hoods/Other Protective Equipment
Specific measures to ensure that fume hoods and other protective equipment are functioning properly and are maintained
How often do you test / inspect to verify flow rate and other parameters?
29 CFR 1910.1450(e)(3)(iii)
Notes: Fume hoods should be used in all operations involving toxic or flammable materials

## Slide 64: Chemical Hygiene Plan Information and Training
Provisions for employee information and training refer to paragraph (f) of the lab standard
For example:
  When will training be provided?
  Who will provide the training?
  How will the training be implemented (format)?
  What will the training include?
29 CFR 1910.1450(e)(3)(iv)
Notes: Safe operation of the laboratory is largely contingent upon personnel awareness and knowledge. It applies to the familiarity with procedures as well as the hazards of chemicals and equipment in the laboratory.

## Slide 65: Chemical Hygiene Plan Prior Approval
Circumstances under which a particular lab operation, procedure, or activity requires prior approval from the employer
Describe when a particular laboratory operation requires prior approval
  Non-routine tasks that may introduce additional hazards into the workplace?
  New methods, analysis?
29 CFR 1910.1450(e)(3)(v)
Notes: Are chemicals procured by the individual or is there a chemical store room?
Mention BASF with the perchloric acid.

## Slide 66: Chemical Hygiene Plan Medical Consultation
Provisions for medical consultation and medical examinations in accordance with paragraph (g) of the lab standard
  Each employee entitled, Why/for what reasons?
  At no cost
  Without loss of pay
  At a reasonable time and place
  Where? When? Who?
29 CFR 1910.1450(e)(3)(vi)

## Slide 67: Chemical Hygiene Plan Chemical Hygiene Officer
Designate who is responsible to implement plan
  May use a committee
    A Chemical Hygiene Officer must be qualified by training or experience, and
    To provide technical guidance in the development and implementation of the provisions of the CHP.
29 CFR 1910.1450(e)(3)(vii)
Notes: The CHO must of have knowledge of chemical health and safety that differentiates the CHO from other safety & health professionals.
Good working knowledge of chemistry and have lab experience.
Still will have a lab manager who has responsibility for their employee’s safety (the CHO facilitates). Also needs good communication skills, and supervisory experience.

## Slide 68: Chemical Hygiene Plan Particularly Hazardous Substances
Provisions for additional employee protection for “select carcinogens”, reproductive toxins, and substances with a high degree of acute toxicity.
  Establish designated area
  Use of containment devices
  Disposal/removal of waste
  Decontamination procedures
Note: This section with (e)(3)(ii) regarding extremely hazardous substances, and (e)(3)(iv) regarding prior approval may all be combined in the CHP.
29 CFR 1910.1450(e)(3)(viii)
Notes: “Select carcinogen” covers a narrower range of substances—any substances regulated as a carcinogen by OSHA, those identified by IARC or NTP, also “potential carc”
Reproductive toxins may manifest themselves as lethal effects on the fertilized egg, developing embryo, or fetus, or teratogenic (malformation) effects in the fetus. Also, some toxins may cause infertility in females AND males.
Acute toxicity examples are: hydrogen cyanide, hydrogen sulfide, and nitrogen dioxide.
1. Designated area is less restrictive and more appropriate for lab operations than the regulated area (which refers to an actual demarcation) as defined in other OSHA standards. It’s purpose is to focus attention on the fact that a particularly hazardous substance is being used and to ensure, where appropriate protective measures are observed by employees working in or near. NOT to restrict large areas of lab space. It may be the entire lab, an area of the lab, or a device such as a hood.

## Slide 69: Chemical Hygiene Plan Review
Review AND evaluate the effectiveness of the Chemical Hygiene Plan at least annually and update as necessary
29 CFR 1910.1450(e)(4)

## Slide 70: Objective 3 Information and Training
Purpose
  To ensure employees are apprised of the hazards of chemicals in their work area
When
  Initial assignment
  Prior to assignments involving new exposure situations
  Frequency of refresher training TBD by the employer
29 CFR 1910.1450(f)
Notes: OSHA proposed that the training and info. Provisions supersede those of the HazCom Std.

## Slide 71: Employee Information
Contents of standard and appendices; shall be made available
Location and availability of Chemical Hygiene Plan
The PELs or RELs (NIOSH) for substances with no OSHA PEL
Informed of What?
29 CFR 1910.1450(f)(3)

## Slide 72: Employee Information
Signs and symptoms associated with exposures to chemicals used in the laboratory
Location and availability of reference materials on hazards, safe handling, storage and disposal, BUT not limited to MSDSs!!
29 CFR 1910.1450(f)(3)(iv)-(v)
Notes: The required training does not necessarily involve training for each specific chemical that the employee will use, but rather the approach may be directed to classes or groups of hazardous chemicals.
** Pertinent reference materials concerning hazards, safe handling, storage and disposal of hazardous chemicals are an essential part of an effective employee protection program. With HazCom, such hazard id is to be provided by the MSDS that accompanies the shipment of the chemical. However, in the event that such info is not received, or is incomplete, or the chemical is generated in the lab, additional reference material is necessary.
***Initially, the proposed lab std only included training on available resources. However, after several groups contested this proposal, OSHA agreed they may have relied too heavily on information which suggested that most lab personnel were already knowledgeable about the hazards related to the chemicals with which they work and the precautions necessary to protect themselves. Even those with advanced degrees are not necessarily trained in the safety and health aspects assoc. with chemical exposures.
There is no restriction on the form in which reference material may be kept, and some er’s may wish to utilize computer technology. This is acceptable as long as employees are aware of procedures necessary to access the information from this source.

## Slide 73: Employee Training
Methods and observations to detect presence or release of hazardous chemical
BOTH physical and health hazards of chemicals used
Methods to protect from hazards inc. specific procedures, work practice, emergency procedures, and PPE
Training shall include WHAT?
29 CFR 1910.1450(f)(4)
Notes: **Although many lab personnel have advanced degrees and are highly competent in their fields of study, that does not make them expert in the hazards associated with chemicals. ***Those with advanced degrees sometimes demonstrate a cavalier attitude towards the potential hazards, and it is important that lab employees receive training to recognize the hazards.
Such as monitoring conducted by the employer, continuous monitoring devices, visual appearance or odor when being released, etc.
Although the proposed standard originally left out training in physical hazards, OSHA realized lab personnel could benefit from this training. Physical hazards are often responsible for subsequent adverse health effects, like explosions and fire could release toxic fumes and vapors. ALSO, failure to provide training on the physical hazards could lead to a false sense of security concerning the range of hazards present.

## Slide 74: Employee Training
The applicable details of the employer’s written chemical hygiene plan, which includes:
  Standard operating procedures
  Prior approval protocols, and procedures for handling select carcinogens, reproductive toxins, and substances with a high degree of acute toxicity (particularly hazardous substances).
29 CFR 1910.1450(f)(4)(ii)
Notes: This differs from the HazCom standard
**For the most part, the training provisions of the lab std are identical to the HazCom Std. There are several additional elements which are specific to the lab std and the chemical hygiene plan in particular.
**Wherever there may be duplication of any requirement, there is no need to perform the function twice. If an employer is complying with the HazCom std, either by choice or necessity, his activities will automatically satisfy any identical requirement of this std.

## Slide 75: Medical Consultation and Medical Examinations
All employees must be provided with an opportunity to receive medical attention, including any follow-up examinations, under the following circumstances:
29 CFR 1910.1450(g)(1)
Notes: The medical consultation is provided for the purpose of determining the need for a medical examination.
Irritation or worse is covered, and medical evaluation needs to be offered.
Stinky odors, discoloration of the skin, etc. are not covered.
Given the multiple chemicals used and the unpredictable exposure situations typical of most lab operations, exposure monitoring was not practical. Additionally, routine medical surveillance was indicated to be prohibitively expensive and have little value because of the wide variety of substances to which workers were exposed, and the difficulty in identifying indicators of adverse health effects.
However, the potential for overexposure still existed, so…

## Slide 76: Medical Consultation and Medical Examinations
An employee develops signs or symptoms associated with chemical
Exposure monitoring reveals an exposure level routinely above the AL or PEL
  For an OSHA regulated substance for which there are exposure monitoring and medical surveillance requirements
  Follow the procedure as prescribed by the particular standard
29 CFR 1910.1450(g)(1)(i)-(ii)
Notes: The proposed standard required employers to provide employees with an exposure evaluation in cases where there was reason to believe an overexposure had taken place. This was not adequate enough for one it relied on the subjective opinion of someone other than the employee that they had been overexposed. It also did not take into account the fact that the employee may feel like they have been exposed, and that they should be allowed to seek medical attention if they had been.
So the final standard incorporates signs or symptoms as a reason for an evaluation.
AND if there appears to be an identifiable condition in terms of overexposure (I.e. exposure levels above the action level (or in case of the absence of an action level, the PEL)

## Slide 77: Medical Consultation and Medical Examinations
Whenever an event such as a spill, leak, explosion, or other occurrence resulting in exposure
Also when...
29 CFR 1910.1450(g)(1)(iii)
Notes: These situations described in these slides should be covered as a minimum in any medical program designed for laboratory workers.

## Slide 78: Medical Consultation and Medical Examinations
Identity of chemical
Description of conditions (inc. quantitative exposure data, if available)
Description of signs and symptoms
Information provided to the physician
29 CFR 1910.1450(g)(3)(i)-(iii)
Notes: All medical exams and consultations shall be provided by or under the direct supervision of a licensed physician, and at a reasonable time and place without cost to the employee.
Problem with trade secrets

## Slide 79: Medical Consultation and Medical Examinations
Physician’s written opinion shall include:
  Any recommendation for medical follow-up
  Results of exams/tests
  Any medical condition revealed that may increase risk as result of exposure to chemical
  A statement that the employee has been notified of findings
  Shall NOT reveal any specific findings
  unrelated to occupational exposure
29 CFR 1910.1450(g)(4)(i)-(ii)
Notes: **Employer must provide all protective measures to that employee, unless physicians deems employee MUST be medically removed.
Existing health impairment may increase health risk, physician should indicate general nature and not specific illness
Written opinion must not reveal specific findings unrelated to occupational exposure.

## Slide 80: Hazard Identification
29 CFR 1910.1450(h)

## Slide 81: Hazard Identification
With respect to labels and MSDSs
  Employers shall ensure that labels on incoming containers are not removed or defaced
  Employers shall maintain any MSDSs received on incoming chemicals and ensure that they are readily accessible
29 CFR 1910.1450(h)(1)
Notes: This action does not represent an increased obligation on employers. They are just to ensure that labels on incoming containers are not removed or defaced. And to retain the MSDSs.

## Slide 82: Hazard Identification
For chemicals developed in the lab
  If chemical is produced exclusively for the lab’s use, and the composition is known, the employer shall provide appropriate training as required by paragraph (f)
29 CFR 1910.1450(h)(2)(i)
Notes: First, if a chemical substance whose chemical composition is known is produced in the lab, for its own use, the available hazard information must be provided to the employee.

## Slide 83: Hazard Identification
For chemical developed in the lab
  Chemical produced is a byproduct whose composition is not known, assume hazardous, and implement paragraph (e) (Chemical Hygiene Plan)
? ? ? ? ?
29 CFR 1910.1450(h)(2)(ii)
Notes: Second, employers who produce a chemical by byproduct whose composition is unknown shall make the assumption that the substance is hazardous, and require it to be handled according to the chemical hygiene plan which provides for appropriate employee protection of chemicals. By following this approach, the employer will not be required to conduct literature searches or perform actual tests to evaluate the hazard.

## Slide 84: Hazard Identification
For chemical developed in the lab
  If chemical is produced for another user outside of the laboratory, the employer shall comply with the Haz Com standard (1910.1200), including the preparation of MSDSs and labeling
29 CFR 1910.1450(h)(2)(iii)
Notes: Finally, with respect with to the substance produced, the employer has become a manufacturer and therefore is subject to all of the relevant provisions of the HazCom std. However, if manu. Is not the lab’s principal concern, the lab std remains in effect for those activities unrelated to the manu. operations

## Slide 85: Use of Respirators
Where the use of respirators is necessary to maintain exposures below the PELs, the employer must comply with the requirements in the respiratory protection standard, 29 CFR 1910.134
29 CFR 1910.1450(i)
Notes: These provisions do not impose any new requirements on laboratory employers, but are included here to remind the employer of the existing compliance duty.

## Slide 86: Recordkeeping
The employer shall establish and maintain an accurate record of any exposure monitoring and medical consultation/ examination
Employer shall ensure records are kept per 1910.1020
Employment plus 30 years
29 CFR 1910.1450(j)(1)-(2)
Notes: Keep records for duration of employment plus 30 years.

## Slide 87: What else do we look for, and Why?

## Slide 88: What else do we look for, and Why?
Please ask for additional information, if interested.
I only included a few extra slides due to the limited time of the presentation.

## Slide 89: General Handling and Storage of Flammable Chemicals
Never heat with an open flame
Do not expose to sources of ignition (electric motors, bunsen burner flames, etc)
All containers must be labeled
Beware of static electricity…
Notes: The one fire we were told about at BASF was due to flammable liquid (ethanol) being heated over an open flame
Static electricity is generated when liquids, esp flammable liquids, move and make contact with other materials, like during pouring, pumping etc. If the static electric charge becomes sufficient enough, a spark can occur from one metal container to the other container and ignite the vapor air mixture.

## Slide 90: General Handling and Storage of Flammable Chemicals
When dispensing flammable liquids (metal to metal), the dispensing container and safety can must be well grounded and bonded

## Slide 91: Specific Hazards of Organic Peroxides
Explosive chemicals
  Some types of peroxides can be handled with relative safety, an insidious and treacherous hazard concerning peroxides is their formation from certain classes of compounds AFTER exposure to air
    Examples:
      1,4-dioxane, ethyl ether, isopropyl
      ether, THF, tetralin, cylcohexane,
      decalin

## Slide 92: Specific Hazards of Ethers…
Explosive chemicals
  Ethyl Ether preferably stored in metal cans
    Inhibited grades can be used longer - no more than 6 months
    Pure, non-inhibited - dispose w/in a few weeks of exposure to air

## Slide 93: Other Hazards: Compressed Gases
Protective caps should be kept on cylinders when not in use
Secured by straps, chains, or stand (more than halfway up the cylinder)

## Slide 94: Other Hazards: Electrical Safety
Grounding
Protect from static electricity
High voltage equipment caged or completely insulated

## Slide 95: Other Hazards: Radiation Safety and Lasers

## Slide 96: Other Hazards: Biological Safety

## Slide 97: Other Hazards: Biological Safety
Containment
  Biosafety Levels (1,2,3,4)
Who’s on First?
Notes: Biosafety level 1
This level is suitable for work involving well-characterized agents not known to consistently cause disease in healthy adult humans, and of minimal potential hazard to laboratory personnel and the environment (CDC,1997).[7]
It includes several kinds of bacteria and viruses including canine hepatitis, non-pathogenic Escherichia coli, as well as some cell cultures and non-infectious bacteria. At this level precautions against the biohazardous materials in question are minimal, most likely involving gloves and some sort of facial protection.
Biosafety level 2
This level is similar to Biosafety Level 1 and is suitable for work involving agents of moderate potential hazard to personnel and the environment.[7] It includes various bacteria and viruses that cause only mild disease to humans, or are difficult to contract via aerosol in a lab setting, such as C. difficile, hepatitis A, B, and C, influenza A, Lyme disease, dengue fever, Salmonella, mumps, measles, HIV,[8] scrapie, MRSA, and VRSA. Genetically modified organisms have also been classified as level 2 organisms, even if they pose no direct threat to humans. This designation is used to limit the release of modified organisms into the environment.
Biosafety level 3
This level is applicable to clinical, diagnostic, teaching, research, or production facilities in which work is done with indigenous or exotic agents which may cause serious or potentially lethal disease after inhalation.[7] It includes various bacteria and viruses that can cause severe to fatal disease in humans, but for which vaccines or other treatment exist, such as Mycobacterium tuberculosis, Bacillus anthracis, West Nile virus, Venezuelan equine encephalitis virus, Eastern equine encephalitis virus, Hendra virus, SARS coronavirus, Salmonella typhi, Coxiella burnetii, Rift Valley fever virus, Rickettsia rickettsii, and yellow fever virus.
Biosafety level 4
This level is required for work with dangerous and exotic agents that pose a high individual risk of aerosol-transmitted laboratory infections, agents which cause severe to fatal disease in humans for which vaccines or other treatments are not available, such as Bolivian and Argentine hemorrhagic fevers, Marburg virus, Ebola virus, Lassa fever, Crimean-Congo hemorrhagic fever, and other various hemorrhagic diseases

## Slide 98: Other Hazards: Biological Safety, cont’d
Pipetting safety
Biosafety cabinet

## Slide 99: Other Hazards: Centrifuge Safety

## Slide 100: Thank You For Attending!
Final Questions?
1-800-NC-LABOR
(1-800-625-2267)
www.nclabor.com
Notes: 100