## Slide 1: N.C. Department of Labor OSH Division
Fundamentals of Noise
Paul M. Sullivan, CIH, CSP
West Compliance Bureau Chief
September 2020
Notes: Rev 0: 6/24/2013

## Slide 2: Objectives
Fundamentals of noise
Anatomy of the ear
Noise measurement instrumentation
Requirements of OSHA’s noise regulation
Enforcement guidelines
Types of hearing loss
Evaluating an audiogram
Proper methods of noise control

## Slide 3: What is Sound?
Defined as a vibratory disturbance in pressure (above and below atmospheric pressure) of a medium which is detectable by the human ear.

## Slide 4: What is Noise?
Defined as sound that carries no information and whose intensity generally varies randomly over time.
Noise is also described as “undesirable / unwanted sound”.

## Slide 5: Wavelength
Measured distance (feet or meters) between two analogous points on two successive parts of a wave.
Greek letter lambda (λ) used to express wavelength.
Number of wavelengths per second equals frequency.

## Slide 6: Frequency
Rate at which variation in normal atmospheric pressure occurs.
Expressed as Hertz (HZ) - synonymous with cycles or waves per second.
Number of waves per second is frequency.

## Slide 7: Human Hearing
Frequency range for young adults with good hearing is usually between 20 - 20,0000 Hz

## Slide 8: Velocity
Velocity at which analogous points on successive parts of a sound wave pass a given point is called the speed of sound (c)
Speed of sound is always equal to the product of the frequency wavelength (c=f)
Speed of sound increases as the medium becomes more dense and less compressible;
  In air at 72° F, c is about 1130 ft/sec
  e.g., c of steel = 16,500ft/sec

## Slide 9: Decibel (dB)
The decibel scale is a logarithmic function named after Alexander Graham Bell.
A dimensionless unit used to express the logarithm of the ratio of a measured quantity to a reference quantity.
Decibels are referenced to 20 micro Newtons/m2 (threshold of hearing at a reference tone of 1000 Hz).

## Slide 10: Why Logarithms???
The ratio between the threshold of pain and the threshold of hearing in humans is 10,000,000.
Therefore a relative scale is more practical than an absolute scale
Using the same ratio on the dB scale is
0 - 140 dB.

## Slide 11: Types of Noise
Continuous noise
  Variations in noise levels are at intervals of 1 second or less.
Impulse/Impact noise
  Less than ½ second in
  duration and do not repeat
  more often than once per
  second.

## Slide 12: Combining Decibels
Difference in dB Values | Add to Higher Value
0 or 1 dB | 3 dB
2 or 3 dB | 2 dB
4 to 9 dB | 1 dB
10 dB or more | 0 dB

## Slide 13: Sound Fields
Free Field
  Uniform sound propagation from a point source with no sound-reflecting obstacles in the sound field.
  Sound pressure level decreases 6 dB for each doubling of distance from the point source (inverse square law)

## Slide 14: Sound Fields
Reverberant Field
  Sound is repeatedly reflected in a room by the walls, floor, and ceiling
  Sound at a given position is made up of direct sound and reflected sound
  Far from the source, the reflected sound dominates, and this region is called the reverberant field

## Slide 15: Sound Pressure Weighting

## Slide 16: A-Weighting
Reduces low frequency noise reception and increases high frequency noise reception.

## Slide 17: C-Weighting
Attempts to measure actual noise levels.

## Slide 18: Typical “A” Measured Sound Levels

## Slide 19: Sound Levels Effects
190 dB | Death
170 dB | Blow out ear drums
160 dB | Deaf in 100 microseconds
120 dB | Pain occurs
115 dB | For 20 min, threshold drop
100 dB | Permanent hearing loss
80 dB | Okay

## Slide 20: Anatomy of the Ear

## Slide 21: Measuring Noise

## Slide 22: Definitions
Criteria Level - Continuous sound level at which the dosimeter will read 100 percent
Exchange Rate - Increment of decibels that requires the halving of exposure time
Threshold - Sound level above which the dosimeter turns on and integrates noise into the measured exposure

## Slide 23: OSHA Exchange Rate
As you increase noise by 5 dB, you must cut exposure in half.

## Slide 24: Noise Instrumentation
Sound level meter
Octave band analyzer
Dosimeter

## Slide 25: Noise Equipment
Sound Level Meter
  Basic instrument to measure sound pressure variations in air.
  Simply a microphone mounted on an amplifier with a meter to indicate the level of sound pressure at the microphone
  ANSI S1.4-1983 Type 2, “Specifications for
  Sound Level Meters”.
  Set at “A” weighting scale, slow response

## Slide 26: SLM Response
TIME CONSTANTS | 
Slow | 1000 milliseconds
Fast | 125 milliseconds
Impulse | 35 milliseconds
Peak | 50 microseconds
NOTE: Human ear averaging time is approximately 30-100 milliseconds | 

## Slide 27: Noise Equipment
Noise Dosimeter
  Instrument which integrates sound pressure over time and directly indicates a noise dose. Used for personal exposure monitoring.
  ANSI S1.25-1978 “Specifications for Noise Dosimeters”.
  90 dBA criterion level, 5 dB exchange rate,
  80 dBA or 90 dBA threshold gate

## Slide 28: Noise Equipment
Octave Band Analyzer
  Instrument used to determine where the noise energy lies in a frequency spectrum. Generally used as a diagnostic tool to help find appropriate engineering controls to reduce noise levels.
  Can be used to evaluate hearing protectors
  ANSI S1.11- 1986

## Slide 29: To Sample or Not?
SLM readings
Duration of exposure (How many hours does equipment run?)
Employee proximity to equipment
Multiple noise sources?
Hearing conservation program?
Complaint?

## Slide 30: Sampling Protocol
Follow the manufacturer’s instruction booklet for proper sampling technique, microphone placement, calibration, charging, etc.
Make sure equipment is properly calibrated and battery function is adequate
Make sure microphone is in employee’s hearing zone

## Slide 31: Sampling Protocol
When noise levels are different for two ears, the higher level must be used
Note situations which can interfere with equipment operation
Obtain at least 5 random SLM readings noting time and job function during reading
Record information as required
on OSHA-92

## Slide 32: Requirements - OSHA’s Noise Regulation
29 CFR 1910.95 – General Industry
29 CFR 1926.52 – Construction Industry

## Slide 33: General Industry
Woodworking
Textiles
Food processing
Machining operations
29 CFR 1910.95

## Slide 34: Hearing Conservation Program
PEL - 90 dBA 8-hour TWA
AL - 85 dBA 8-hour TWA
Maximum exposure (for example) - 115 dBA for 15 min
Maximum impact or impulse noise - 140 dBA
  How can this be measured?
  When would you cite it?
29 CFR 1910.95(a)-(b)

## Slide 35: Hearing Conservation Program
If exposures exceed 90 dBA as an 8-hour TWA
  Feasible administrative or engineering controls shall be utilized.
  If such controls fail to reduce sound levels to below the PEL, PPE shall be provided and used.
29 CFR 1910.95(b)

## Slide 36: Hearing Conservation Program
Employer shall administer a continuing effective hearing conservation program when noise exposures equal or exceed an 8 hour TWA of 85 dBA.
  Does this program have to be in writing?
In determining exposure, no regard is given to hearing protector attenuation.
  Where does hearing protection attenuation
  come into play?
29 CFR 1910.95(c)

## Slide 37: Monitoring
Develop a monitoring program
Develop a sampling strategy
29 CFR 1910.95(d)

## Slide 38: Monitoring
Is dosimetry required?
Can an employer comply with (d) by using an SLM?
  How?
29 CFR 1910.95(d)

## Slide 39: Employee Notification
Employer shall notify each employee exposed at or above 85 dBA of the monitoring results.
  How would you recommend this be accomplished?
29 CFR 1910.95(e)

## Slide 40: Audiometric Testing Program
Establish and maintain an audiometric testing program.
Baseline audiogram
Mobile test van exception
NOTE: Audiograms should be preceded
by 14 hours without workplace noise
exposure
29 CFR 1910.95(g)

## Slide 41: Audiometric Testing Program
Follow-up procedures
Revised baseline
Standard threshold shift
29 CFR 1910.95(g)

## Slide 42: Audiometric Test Requirements
This section sets the criteria for how the tests should be conducted and what standards audiometric test equipment shall meet.
29 CFR 1910.95(h)

## Slide 43: Hearing Protectors
Shall be available to employees exposed at or above 85 dBA
Shall be required for those employees:
  Exposed at or above 90 dBA
  Exposed at or above 85 dBA (no baseline)
  Who have an STS
29 CFR 1910.95(i)

## Slide 44: Hearing Protector Attenuation
Hearing protectors shall:
  Attenuate to an 8 hour TWA PEL of 90 dBA
  Attenuate to an 8 hour TWA PEL of 85 dBA, for those with a STS
  Be reevaluated whenever noise exposures increase to determine adequacy.
29 CFR 1910.95(j)

## Slide 45: Training
Shall be instituted for employees exposed at or above 85 dBA
Shall be repeated at least annually, or as needed and include:
  Effects of noise on hearing
  Purpose of hearing protectors
  Instruction and proper selection, fitting,
  use, and care
  Purpose of audiometric test and
  explanation of the procedures and
  results.
29 CFR 1910.95(k)

## Slide 46: Construction Noise Sources
Earth moving equipment
Power tools (nail guns, etc.)
Abrasive blasting
Jack hammers
Air compressors
Pneumatic nail guns, staple guns
Confined space
29 CFR 1926

## Slide 47: Construction Industry
Hearing Conservation Program required at 90 dBA
  What is required in a construction hearing conservation program?
29 CFR 1926

## Slide 48: Enforcement Guidelines

## Slide 49: Noise Enforcement
Refer to Technical Manual Section II: Chapter 5
Use 80 dBA threshold for Hearing Conservation
Use 90 dBA threshold for PEL
Use SLM for impact noise

## Slide 50: Interpreting Dosimeter Readings Using 80dBA Threshold Level
Dosimeter Reading | Compliance with PEL | Compliance with AL
<50% | Within PEL | Within Al
50% - 66% | Within PEL | Inconclusive
>66% | Within PEL | Over AL

## Slide 51: Interpreting Dosimeter Readings Using 90dBA Threshold Level
Dosimeter Reading | Compliance with PEL | Compliance with AL
<50% | Within PEL | Inconclusive
50% - 66% | Within PEL | Inconclusive
66% - 100% | Within PEL | Over AL
100% - 132% | Inconclusive | Over AL
>132% | Over PEL | Over AL

## Slide 52: Noise Enforcement
Pre and post- calibrate equipment
Take at least 5 random SLM readings
Obtain information for OSHA-92
Take appropriate photographs
Note types and NRR of hearing
protection used; is it being used
properly?

## Slide 53: Noise Enforcement
Note type and location of noise sources adjacent to employee sampled
Copy data before you leave site
Note breaks, lunch hours, machine down time
Typical work day?

## Slide 54: Noise Enforcement
Hearing Protector Attenuation - Compliance:
NRR-7 (for spectral uncertainty)
Approximately Field Attenuation - Recommend
NRR-7 X 50%
Dual protection: (NRR -7) + 5
Note: NRR is for higher-rated protector

## Slide 55: Noise Enforcement
Serious Citation - Exposure Dose 132% and:
  HP not provided or utilized correctly and/or
  HCP is deficient or non-existent
“Other” Citation - Exposure Dose 66% and:
  HCP is non-existent or deficient in some element
Note: If effective HP, HCP and no feasible administrative or engineering controls exist, then no citation will be issued.

## Slide 56: Insertion of Ear Plugs

## Slide 57: Types of Hearing Loss

## Slide 58: Types of Hearing Loss
Conductive hearing losses
  Wax build-up
  Foreign objects
  Infections
  Rupture of ear drum
  Accidents with sharp blow to head
  Some medical conditions

## Slide 59: Types of Hearing Loss
Sensori-neural hearing loss
  Presbycusis
  Disease
  Ototoxic drugs
  Noise-induced hearing loss

## Slide 60: Noise-Induced Hearing Loss
Immediate acoustic trauma
  Cochlear structures are mechanically broken apart by the pressure wave
  Extremely intense sound levels
  Gradually progressive
  Temporary threshold shift
  Permanent threshold shift

## Slide 61: Degree of Hearing Loss

## Slide 62: Auditory Effects of Noise
Temporary effects
  Interference with communication and perception of warnings
Permanent effects
  Tinnitus, recruitment
  Safety concerns
  Social isolation

## Slide 63: Evaluating an Audiogram

## Slide 64: Evaluating an Audiogram
Check for baseline audiogram
Evaluate for threshold shift in the 2,000/3,000/4,000 Hz range
If average of shift in above range is 10dBA then a STS has occurred (apply age correction if necessary).
Check 200 Logs for STS.

## Slide 65: Audiometric Examination Report

## Slide 66: Normal Hearing

## Slide 67: Sensorineural Hearing Loss

## Slide 68: Conductive Hearing Loss

## Slide 69: Proper Methods of Noise Control

## Slide 70: Noise Control
Noise engineering controls
  Replacement
  Source modification
  Path modification

## Slide 71: Noise Control
Replacement
  Quieter equipment
  Quieter processes
  Quieter materials
Notes: Professional noise control and ventilation for turbines Professional noise control and ventilation for turbines Professional noise control and ventilation for turbines

## Slide 72: Noise Control
Source modification
  Reduce driving force
  Reduce response of vibrating surface
  Reduce area of vibrating surface
  Use directivity of source
  Reduce velocity of fluid flow
Notes: Vibration switches and monitors minimize production shut down time and repair costs by measuring the total accelerated force (shock) present on a machine. Individual acceleration measurements are summed to yield the total destructive force acting on a machine.

## Slide 73: Noise Control
Path modification
  Enclosures
  Shields of barriers
  Room absorption
  Lined ducts and mufflers

## Slide 74: Air Noise
Approximately 50% of all high noise sources are due to compressed air
Generally in the 2000 Hz to 8000 Hz bands
Can be controlled below 90
dB in nearly all cases
Most common sources are
blow-offs and pneumatic
valves

## Slide 75: Duct Silencers

## Slide 76: Compressed Air Silencer

## Slide 77: Pneumatic Muffler

## Slide 78: Air Silencers and Vibration Mounts

## Slide 79: Noise Curtains

## Slide 80: Expansion Joints/Fan Connector

## Slide 81: Sound Absorption Baffles and Wall Panels

## Slide 82: Resources
OSHA Technical Manual
FIS (search DOL intranet)
Internet (USDOL, NIOSH, etc.)
Library (check DOL intranet)

## Slide 83: Resources
NIOSH Technical Report - Compendium of Materials for Noise Control (80-116)
NIOSH Criteria for a Recommended Standard (98-126)
Noise and Hearing Conservation Manual
(Berger,Ward, Morrill, Royster; 4th edition)

## Slide 84: Case Studies

## Slide 85: Case Studies
For each of the following case studies:
  What OSH violations are present?
  What is the hazard?
  Which employees are exposed?
  How many?
  What is the assessed severity
  and probability?
  What are some abatement recommendations?

## Slide 86: Case Study #1 – Groups 1 & 2
Employees at a yarn manufacturing facility are exposed to noise in various departments including carding, drawing, roving, and spinning.
The facility operates three 8-hour shifts each day.
Employees operate the textile machinery and wear EAR foam ear plugs as shown in the following photos.
Audiograms were conducted for a few employees three years ago, but none since.
The company has a written hearing conservation program.
  Noise monitoring was conducted with Type-2 Quest Dosimeters

## Slide 87: Case Study #1
Dose | Employee #1 Carding | Employee #2 Maintenance | Employee #3 Roving | Employee #4 Ring Spinning
Dose – LTL | 120.75 | 53.24 | 75.8 | 199.12
Dose – HTL | 99.6 | 39.15 | 59.2 | 172.31
Lavg – LTL | 91.64 | 87.07 | 88.2 | 94.84
Lavg – HTL | 90.3 | 84.84 | 86.4 | 93.78
Ltwa – LTL | 91.4 | 85.52 | 88.0 | 95.03
Ltwa – HTL | 90.03 | 83.3 | 86.2 | 93.98
Peak | 143 | 128.6 | 118.2 | 123.0
Run Time | 7:41 | 6:25 | 7:44 | 8:09

## Slide 88
Case Study #1

## Slide 89
Case Study #1

## Slide 90
Case Study #1

## Slide 91
Case Study #1

## Slide 92
Case Study #1

## Slide 93: Case Study #2 – Groups 1 & 2
Three employees operate a corrugating machine at a cardboard manufacturing plant.
One 8-hour shift is utilized, and the company has a full hearing conservation program.
The company says they are aware of the noise problem, but that it will cost about $600,000 to enclose the corrugating machine.

## Slide 94: Case Study #2
Dose | Machine Operator
Dose – LTL | 376.45
Dose – HTL | 374.24
Lavg – LTL | 99.56
Lavg – HTL | 99.52
Ltwa – LTL | 99.56
Ltwa – HTL | 99.52
Peak | 115.4
Run Time | 8:00

## Slide 95: Case Study #3 – Groups 1 & 2
Employees at a small woodworking shop operate a variety of machines in the manufacture of table legs.
The company has no hearing conservation program.
Employees work four ten-hour shifts each week.

## Slide 96: Case Study #3
Dose | Lathe Operator | Sander
Dose – LTL | 169.24 | 138.94
Dose – HTL | 137.20 | 112.42
Lavg – LTL | 92.25 | 90.97
Lavg – HTL | 90.73 | 89.44
Ltwa – LTL | 93.80 | 92.37
Ltwa – HTL | 92.28 | 91.45
Peak | 114.7 | 120.8
Run Time | 9:55 | 9:43

## Slide 97
Case Study #3

## Slide 98
Case Study #3

## Slide 99
Case Study #3

## Slide 100
Case Study #3

## Slide 101: Case Study #4 – Groups 3 & 4
Employees operating jet and atmospheric dye machines at a textile dyeing and finishing plant are exposed to noise throughout their 8-hour shifts.
The company has a partial hearing conservation program.
Ear plugs are provided, but generally not used by employees (and not required).
Audiograms are conducted annually when the test van comes to the plant.
The OSHA 300 logs showed 3 STS’s (out of 40 Dye Room employees tested).
Monitoring by the HCO was shorted by about 90 minutes when the employee sampled went home sick.

## Slide 102: Case Study #4
Dose | Jet Dye Machine Operator | ATM Dye Machine Operator
Dose – LTL | 56.45 | 64.84
Dose – HTL | 12.41 | 9.54
Lavg – LTL | 87.37 | 86.92
Lavg – HTL | 76.44 | 73.10
Ltwa – LTL | 85.88 | 86.87
Ltwa – HTL | 74.95 | 73.05
Peak | 109.8 | 112.4
Run Time | 6:30 | 7:57

## Slide 103: Case Study #5 – Groups 3 & 4
Employees at a paper recycling plant shred and re-bale cardboard and wastepaper for sale to other companies.
The workers feed paper onto the conveyor and it is dumped into the shredder.
Hearing protection was not worn on the first day of the inspection but was used during the noise monitoring.
No other elements of a hearing conservation program were in place.
Some of the laborers in this area were working for a temp company and had been there for about a 1 ½ months.

## Slide 104: Case Study #5
Dose | Baler | Laborer | Laborer
Dose – LTL | 91.0 | 157.8 | 161.8
Dose – HTL | 62.9 | 144.3 | 147.6
Lavg – LTL | 89.4 | 93.5 | 93.6
Lavg – HTL | 86.7 | 92.8 | 92.9
Ltwa – LTL | 89.3 | 93.3 | 93.5
Ltwa – HTL | 86.7 | 92.6 | 92.8
Peak | 126.7 | 135.0 | 132.7
Run Time | 7:57 | 7:55 | 7:59

## Slide 105
Case Study #5

## Slide 106
Case Study #5

## Slide 107
Case Study #5

## Slide 108
Case Study #5

## Slide 109: Following Abatement

## Slide 110
Following Abatement

## Slide 111
Following Abatement

## Slide 112
Following Abatement

## Slide 113: Case Study #6 – Groups 3 & 4
Employees at a road construction site are operating a rock drill.
They utilize ear plugs properly (NRR=24) and receive baseline audiograms.
However, annual audiograms, initial monitoring, and training are not conducted.
Exposure monitoring showed a Dose-HTL of 627% as measured over 8 hours.

## Slide 114
Case Study #6

## Slide 115: Thank You For Attending!
Final Questions?
1-800-NC-LABOR
(1-800-625-2267)
www.nclabor.com