## Slide 1: N.C. Department of Labor OSHA 125 Course
29 CFR 1910.1025 Lead Standard
29 CFR 1926.62 Lead Standard
Notes: Rev 0: 6/24/2013

## Slide 2: Lead Stuff
We don’t eat lead paint chips!
  We consume lead dust, its easier to swallow
  Same with children
Lead interacts with our bodies
  Word

## Slide 3: What Industries?
Battery manufacturing Chemical industry Construction workers Demolition workers Firing-range instructors Foundry workers Gas-station attendants Gasoline additives production Jewelers Lead miners Lead smelters and refiners
Pigment manufacturing Pipe fitters Plastics industry Pottery workers Printers Radiator repair Rubber industry Soldering of lead products Solid waste production Stained-glass makers Welders

## Slide 4: With Pictures!
Radiator repair shops
Storage batteries
Paints, dyes, ceramics
Foundries
Manufacturing of ammunition
Firearm ranges
Electronics
Weights
Notes:   Highly toxic heavy metal.

## Slide 6: Lead Standard
Objectives
  To list the general requirements of the lead standard
  To apply the lead standard to data obtained during inspection activity
  To identify the differences between the general industry and construction lead standards
  Gain the tools necessary for an inspection with lead.
29 CFR 1910.1025
29 CFR 1926.62
Notes: NOTE: Tech Manual sect V, chap 3 about controlling lead in construction
Objectives:
-to list the general requirements of the lead standard.
-to apply the lead standard to data obtained during inspection activity
-to identify the differences between the General Industry and Construction lead standards.

## Slide 7: Why the Fuss?
The list below shows many of the key lead-induced health effects.
Neurological Effects
  Peripheral neuropathy
  Fatigue / Irritability
  Impaired concentration
  Hearing loss
  Wrist / Foot drop
  Seizures
  Encephalopathy
Gastrointestinal Effects
  Nausea
  Dyspepsia
  Constipation
  Colic
  Lead line on gingival tissue
Reproductive Effects
  Miscarriages/Stillbirths
  Reduced sperm count & motility
  Abnormal sperm
Heme Synthesis
  Anemia
  Erythrocyte protoporphyrin elevation
Renal Effects
  Chronic nephropathy with proximal tubular damage
  Hypertension
Other
  Arthralgia
  Myalgia

## Slide 8: Illness
Encephalopathy - means disorder or disease of the brain
Dyspepsia – upset stomach
Anemia – is a condition in which the body does not have enough healthy red blood cells.
Nephropathy – refers to damage to or disease of the kidney.

## Slide 9: General Industry
1910.1025
Flip in your books to this section.
Reviewing the basics of the standard.

## Slide 10: Construction
1926.62 – Lead
Flip in your books to this section.
Reviewing the basics of the standard.

## Slide 11: Lots of information
Good news: 95% is the same
Bad news: still have to carry two books
Bad news: still have to know both
Good news: We have till 5:00 to get it done

## Slide 12: Breakdown: 1910.1025
(a) Scope
(b) Definitions
(c) Permissible Exposure Limits (PEL’s)
(d) Exposure Monitoring
(e) Methods of Compliance
(f) Respiratory Protection
(g) Protective Work Clothing

## Slide 13: Breakdown: 1910.1025 cont.
(h) Housekeeping
(i) Hygiene Facilities and Practices
(j) Medical Surveillance
(k) Medical Removal Protection
(l) Employee Information and Training
(m) Signs
(n) Recordkeeping
(o) Observation and Monitoring

## Slide 14: Breakdown: 1926.62
(a) Scope
(b) Definitions
(c) Permissible Exposure Limits (PEL’s)
(d) Exposure Assessment
(e) Methods of Compliance
(f) Respiratory Protection
(g) Protective Work Clothing

## Slide 15: Breakdown: 1926.62 cont.
(h) Housekeeping
(i) Hygiene Facilities and Practices
(j) Medical Surveillance
(k) Medical Removal Protection
(l) Employee Information and Training
(m) Signs
(n) Recordkeeping
(o) Observation and Monitoring

## Slide 16: Appendices
Appendix – A (read I)
Appendix B – (In a nut shell)
Appendix C – Medical Surveillance (Pb 101 in the body)

## Slide 18
The Quick look – is it lead?

## Slide 24: The Scenario
We will be discussing a scenario throughout the training. Provided 2 case files at the end.
Pull the information we have learned
Create a guideline for future inspections
Questions – ask as we go!

## Slide 25: Inspection Time
You are given an inspection. Employees are removing pain from a water tower.
Media reports that the project will take approximately 8 weeks in total.
First thoughts?

## Slide 26: Inspection Time
Lets start with Construction
What are our questions:
  1) has lead been identified?
  2) are we generating air borne dust?
    what does this?
    Why is this important?
If both are true what’s first?

## Slide 27: Lead – 1926.62
Exposure Assessment:
  1926.62(d)
The A’s and the B’s
Make a note! (d) – is where it all begins.

## Slide 28: Inspection
After interviewing our Contractor we know:
  Sandblasting occurred on the legs and shell
  3 people inside,
    All three with a hood
    All 3 wear a half mask respirator when exiting the containment
Based on our activities what do we expect to see?
Where do we begin?

## Slide 29: Exposure Assessment
Tasks?
Respirators?
Blasting employee needs what?
Clean up employees need what?
So many questions!

## Slide 30: Methods of Compliance??
For construction you have to review section 62.d first, and is mostly where you will cite.
For industry you have to review 62.e, and is mostly where you will cite.
The rest of the standard supports these two areas.

## Slide 31: 1926.62(v) – The project
A – respirators (f)
B – PPE (g)
C – Change areas (i2)
D – Hand washing (i5)
E – Biological Monitoring (j)(1)(ii)
F – training (l)(1)(i)

## Slide 32: But we are sampling right now!
Now that we have that covered – lets move on to the rest of the standard!
Following our (d)(2)(v)
  PPE

## Slide 35: Lead PPE 1926.62(g)
Full body work clothing
Protect the rest
So what did our workers have?
  Full body work suits
  Respirators
  Gloves
  Shoes (work boots)
Contamination?

## Slide 36: Hygiene Concerns
Potable water?
Wash station, shower?
No eating, drinking, no tobacco (including chew!!) or cosmetics
  Cosmetics?

## Slide 37: Water?

## Slide 38: Hygiene Continued 1926.62(i)
Change Areas
Showers
  Shower facilities actually no garden hose for you!
  Where feasible?
  Supply cleaning agents and towels!
Clorox wipes a good idea?

## Slide 39: Washing Hands
A whole slide on washing hands?
The other lead case!
Wash your hands.
Remember Routes of Entry

## Slide 41
Notes: Hand washing facility.

## Slide 42: Lead Standard
All medical exams and procedures provided at no cost to employees at a reasonable time and place.
Basics of medical Surveillance
  Read the details
    What's the difference between (1)(i) and (1)(ii)
  J(2) – That’s specific
    Need records, dates, work history
Notes: (j)(1)(iii) Q: Do employees get paid while they are going for medical exams? A: Yes.

## Slide 43: Medical Surveillance 1926.62(j)
Not your vitals, your lead and zinc protoporphyrin levels!
Biological monitoring
  Blood Pb sampling and analysis
    Every 6 mo. when over the AL 30 days/year
    Every 2 mo. when blood Pb is 40 g/100g
    Every month when on removal for blood Pb

## Slide 44: ZPP at a glance
Why Get Tested?
To screen for and monitor chronic exposure to lead; to detect iron deficiency in children
When to Get Tested?
When you have been chronically exposed to lead, as part of a program to monitor lead exposure, and/or when your doctor suspects lead poisoning; as part of a screening program for iron deficiency in children and adolescents
Sample Required?
A blood sample drawn from a vein in your arm or from a fingerstick

## Slide 45: Lead Standard -Medical
Follow-up blood sampling tests when the criterion for removal is reached 50 g for construction (60 g once or 50 g as 6 month average for General Industry)
Employee notification
Notes: 45

## Slide 46: Lead Standard -Medical
Medical exams prior to a Pb assignment
Medical exams will include detailed work and medical histories and a thorough physical examination.
Notes: 46

## Slide 47: Lead Standard -Medical
Multiple physician review allowed
Information about the job (airborne levels, PPE, employee duties) and blood Pb levels must be provided to the physician
Notes: 47

## Slide 48: Lead Standard -Medical
The physician must provide a written medical opinion for the employee.
Chelation is permitted only in a clinical setting with physician supervision.
Notes: 48

## Slide 49: Lead Standard -Medical
Temporary medical removal from jobs over the AL for:
  Construction EE at 50 g/dl
  Employees with blood Pb at 60 g/dl
  Employees with 6 month average blood Pb at 50 g/dl.
Temporary medical removal from jobs over the AL due to medical determination.
Notes: 49

## Slide 50: Lead Standard -Medical
Return to former job when:
  Two consecutive blood Pb are below 40 g/dl (for both standards)
  With physician determination of improved health
Notes: 50

## Slide 51: Lead Standard -Medical
Removal benefits are specified
Follow up medicals specified
Worker compensation applies
Notes: 51

## Slide 52: Training 1926.62(l)
Have to train each employee who is subject to exposure to lead at or above the AL
Has to be provided prior to employment
And annually to all employees who are subject to lead exposure at or above the AL on any day.
Example of an employee that would not be trained?

## Slide 53: Training Cont.
Training Programmed spelled out:
  1926.62(l)(2)
What does 1926.62(l)(3)(ii) mean?

## Slide 54: Training cont
All employees exposed to Pb to be trained on Appendices A and B
  Appendix A
    Substance data sheet for occupational exposure to lead
  Appendix B
    Employee standard summary

## Slide 55: Lead Standard
All employees exposed over the AL to have in depth training on an annual basis and prior to initial assignment
  Contents of standard and appendices
  Jobs with exposures over the AL
  Medical surveillance
  Engineering and other controls
  Compliance plan

## Slide 56: Signs 1926.62(m)
Your right, not part of the list
But – it goes along with training
1926.62(m)(2)(i)
  That’s the sign.
Check out 2(ii) – Illuminated and Cleaned!

## Slide 57: The sign
WARNING LEAD WORK AREA POISON NO SMOKING OR EATING

## Slide 58: Recordkeeping 1926.62(n)
This is in that list.. Where else are you going to find all that information?
What does (1)(i) say?
How long to keep?
  1926.62(n)(1)(iii)
  Hint- 1910.1020(d)

## Slide 59: A Note
Objective Data and Previously monitored in 12 months!
Be extra critical, be extra cautious.
1926.62(d)(4) – Positive initial monitoring
1926.62(d)(5) – Negative initial determination

## Slide 60: Lead Standard
Air Monitoring Data Review
29 CFR 1910.1025

## Slide 61: Are we done?
Nope, but ½ way I think – onto the evaluation of their controls.
We are BACK to that pesky (e)!
  The down and dirty.
Methods of Compliance.. Its all spelled out.

## Slide 62: Lead Standard Still at e
Engineering and work practice control requirements:
  Over PEL 31 or more days, reduce exposure to below the PEL OR as low as feasible and use APPROPRIATE respirators.
  Over PEL 30 or fewer days, reduce
  exposure to 200  g/m3 and use
  respirators to maintain exposures
  to below the PEL
Notes: Feasibility discussion (look at Ch 15 of FOM):
Technical feasibility: similar situations observed, methods documented in journals or at conferences, studies from a qualified professional (consultant), equipment catalogs or suppliers.
Economic feasibility: cost is not usually considered (except in contestment), however, if it places an undue burden on the employer and would “shut the doors”, an extended abatement date can be set. The BC must approve abatements longer than 1 year. It is recommended that the employer provide periodic updates on work done during these longer abatements.

## Slide 63: What respirator?
At minimum what should you expect an employee to be wearing?
  Table 1 (1910.134)
Cartridges?
What about the respirator standard?
One more list to follow!

## Slide 64: Lead Standard Still at e
When engineering and work practices controls do not reduce exposure below the PEL, use respirators per paragraph (f)
Establish / implement a written plan to comply with PEL
  Revise every 6 months
Seriously! Take a look.
  A through I
Notes: These are to be made available to the Asst Sec, the Director, and any affected employees or authorized employee reps for examination and copying.
Asst Sec is anyone from OSHA, Director is anyone from NIOSH
EE reps are union reps or stewards, spouses, parents, children, lawyers, MDs, etc.

## Slide 65: This is mostly identical in both standards
  Describe each operation
  Describe specific means of compliance
  Report the technology considered
  Document emission sources with IH data
  Detail time schedule for implementation
  List work practices required in (g), (h), (i)
  Describe administrative control schedules
  Document other relevant information

## Slide 66: Guess where?
1926.62(e)(2)(ii)(H) – for all the multi-contractor sites.
Check out 1926.62(e)(2)(iii)
  Required!
Moving right along…. Jumping around…

## Slide 67: Lead Standard
Mechanical ventilation
  Effectiveness checks required every 3 months and after any change in process that might alter employee exposures.
  Any recirculated air must be HEPA filtered and monitored.
    Pb in the return air must cause automatic bypass of the system
Notes: Ventilation checks: capture velocity, duct velocity, static pressure.

## Slide 68: Lead Standard
Administrative control documentation for employee rotation
  Name or ID number of each affected employee
  Duration and exposure levels at each job
  Any information useful for assessing that these controls reliably reduce employee exposure

## Slide 69: Lead Standard
Respirators must be worn when necessary to install and/or implement engineering/ work practice controls or when those controls are not sufficient to reduce exposures to below PEL.
The employer must implement a respiratory protection program in accordance with 29 CFR 1910.134.

## Slide 70
29 CFR 1910.1025
Lead Standard
Notes: respirator storage, Company J

## Slide 71: Lead Standard
The employer provides for cleaning or disposal of protective clothing and equipment
The employer is to repair and replace equipment as needed

## Slide 72: Lead Standard
Back to General industry:
Can you eat in your lead clothes?
Placed in closed container to
prevent spread of lead dust.
Remember the Indoor lead case?

## Slide 73: Lead Standard
Notify the laundry in writing re: Pb contamination and potential health effects.
Containers must be labeled.
Shaking or blowing off with compressed air to clean PPE is prohibited.
Notes: Pb overexposures have been documented in the laundry areas of uniform service companies.

## Slide 74: Lead Standard
Surfaces free of Pb accumulations.
  Use 200 g/ft2 per CPL 2-2.58 (1926.62)
Do not used compressed air to clean floors. Shoveling and dry sweeping to be used only where vacuuming not effective.
  Vacuums to be used and emptied to keep recontamination to a minimum.

## Slide 75
Lead Standard
29 CFR 1910.1025
Notes: lead oxide is leaking from ball mill, Company J

## Slide 76
Lead Standard
29 CFR 1910.1025
Notes: company using a dust reducing compound in house keeping, Company V

## Slide 77
Lead Standard
29 CFR 1910.1025
Notes: Vacuum, Company V

## Slide 78
Lead Standard
29 CFR 1910.1025

## Slide 79
Lead Standard
29 CFR 1910.1025
Notes: Vacuum, Company J

## Slide 80
Lead Standard
29 CFR 1910.1025
Notes: uniform storage, Company V

## Slide 81: Lead Standard
Shower facilities (per 1910.141(d)(3)) provided with Pb over PEL. Must shower at end of shift, can’t leave wearing Pb contaminated work clothes.

## Slide 82: Lead Standard
Lunchrooms provided when over PEL
  Must have a temperature controlled, positive pressure, filtered air supply.
  Must wash prior to eating, drinking, smoking.
  Must remove surface dust from PPE by vacuum or downdraft booth.
Restrooms must be provided per 29
CFR 1910.141

## Slide 83: Lead Standard
Employees can observe monitoring
Effective date – March 1, 1979
Appendices to supplement standard

## Slide 84: Back to our Job
Handout of 1A
Lets do the inspection:
You lead the questions!

## Slide 85: Show Case Pictures
Gun Manufacturing - GI
  Review case pictures
  Review case file
Water Tank – Con.
  Review case pictures
  Review case file

## Slide 86: What Else but CPL’s
CPL 2-2.46 – Medical Records review
CPL 2-2.33 – OSHA Access to Employee Medical records
CPL 2-2.58 Lead In Construction
CPL 2-2.67 lead Brass & Bronze Ingot Manufacturing
CPL 03-00-009 NEP Lead

## Slide 87: Thank You For Attending!
Final Questions?