## Slide 1: N.C Department of Labor OSH Division
Sampling and Analysis
Presented by: ETTA Bureau, (919) 707-7876

## Slide 2: Resources
FOM Chapter XV – Industrial Hygiene Compliance
  OneStopShop
OSHA Technical Manual
  https://www.osha.gov/dts/osta/otm/otm_toc.html
Chemical Sampling Information – OSHA website
  https://www.osha.gov/dts/chemicalsampling/toc/toc_chemsamp.html
NIOSH – Occupational Exposure Sampling Strategy Manual
  http://www.cdc.gov/niosh/docs/77-173/
Patty’s Industrial Hygiene and Toxicology

## Slide 3: Objectives
Discuss Sampling Equipment
Describe Analytical Techniques
Reasons for Sampling
Develop Sampling Strategy
Evaluation of Sampling Results
Carbon Monoxide – Coburn Equation
Common Citations

## Slide 4: Brief Review

## Slide 5: Hazard Categories for IHs
Condition
Thermal
  Hot
  Cold
Ergonomic
  Vibration
  Repetitive tasks
Noise
  Continuous
Contaminant
Chemical
  CO
Biological
  Mold
Radiation
  Ionizing
  Non-ionizing
Reactive (explosive)
  Combustible dust

## Slide 6: Classification of Airborne Contaminants
Physical State
Solids
  Fumes
    Particles formed by condensation of vapor, generally after volatilization from the molten state and can be accompanied by a chemical reaction.
      Size range: 0.01µm – 10.0µm
  Dusts
    Particles generated by mechanical action.
      Size range: 1µm – 100µm
  Fibers
    Particulate with an aspect ratio (length to width) of 3:1

## Slide 7: Classification of Airborne Contaminants
Physical State
Liquids
  Mists
    Suspended liquid droplets generated by condensation (from gas to liquid).
      Size range: 0.01µm – 10µm
Gases
  Vapors
    A gaseous form of a substance that is normally a solid or liquid at room temperature

## Slide 8: Classification of Airborne Contaminant
Multiple Physical States
Aerosol
  Liquid droplets or solid particles dispersed in air.
    Size range: 0.001µm – 50µm
Particulate matter
  Fine solid or liquid particles dispersed in air.
Smoke
  Contains liquid droplets, solid particles, and gases originating from incomplete combustion.
    Size range: 0.01µm – 1.0µm

## Slide 9: Routes of Entry
Inhalation
  Material enters the body by breathing.
Ingestion
  Material enters the body by swallowing.
Absorption
  Material enters the body by diffusing across tissue/membranes.
Injection
  Material enters the body when tissue/membranes are punctured or broken.

## Slide 10: Toxicological Classification
Different criteria used throughout the world
Examples:
  Acute Toxicity
  Asphyxiants
  Carcinogens
  Chronic Toxicity
  Corrosive
  Irritation
  Mutagens
  Reproductive Toxicity
  Sensitization
  Systemic Poisons
  Teratogens

## Slide 11: Physiological Effects
Acute Toxicity
  Refers to those adverse effects occurring following oral or dermal administration of a single dose of a substance, or multiple doses given within 24 hours, or an inhalation exposure of 4 hours.
    e.g., phenol – [C6H6O]; nickel carbonyl – [Ni(CO)4]
Chronic Toxicity
  Refers to the ability of a chemical to do systemic damage as a result of many repeated exposures, during a prolonged period of time, to relatively low levels of the chemical.
    e.g., phenol – [C6H6O]; nickel carbonyl – [Ni(CO)4]

## Slide 12: Physiological Effects
Systemic Poisons
  Toxic substance whose effect is not localized in one spot but spreads to all body organs and systems in varying degrees, the major effects being manifested in one or two organs.
    e.g., tetraethyl lead – [(CH3CH2)4Pb]

## Slide 13: Physiological Effects
Asphyxiants
  A vapor or gas that can cause unconsciousness or death by suffocation due to lack or depletion of oxygen.
    Simple asphyxiants
      Are inert gases or vapors which are harmful to the body when they become so concentrated that they reduce oxygen in the air to dangerous levels
        e.g., carbon dioxide – [CO2]; nitrogen – [N]; methane – [CH4]; hydrogen – [H]
    Chemical asphyxiants
      Cause suffocation by either preventing the uptake of oxygen in the blood or by preventing the normal oxygen transfer from the blood to the tissues or within the cell itself.
        e.g., carbon monoxide – [CO]; hydrogen cyanide – [HCN]; hydrogen sulfide – [H2S]

## Slide 14: Physiological Effects
Corrosive
  Chemical at the site of contact that causes visible destruction or irreversible alterations of the skin, eyes, lining of the respiratory tract, or gastrointestinal tract.
    e.g., hydrochloric acid – [HCl]; sulfuric acid – [H2SO4]
Irritation
  Chemical at the site of contact may cause inflammation of the skin, eyes, lining of the respiratory tract, or gastrointestinal tract.
    e.g., ammonia – [NH3]; nitrogen dioxide – [NO2]

## Slide 15: Physiological Effects
Mutagens
  Chemicals to modify the genetic material in the nucleus of cells in ways that allow the changes to be transmitted during cell division and potentially causing heritable effects.
    e.g., bromine – [Br]; benzene – [C6H6]
Carcinogens
  A substance or a mixture of substances which induces cancer or increases its incidence.
    e.g., Beta-naphthylamine – [C10H9N]; Bis-chloromethyl either (BCME) – [C2H4Cl2O]

## Slide 16: Physiological Effects
Reproductive Toxicity
  Adverse effects induced by a chemical on any aspect of mammalian reproduction.
    Reproductive Toxicity
      Adverse effects that interfere with the ability of males or females to reproduce.
        e.g., lead – [Pb]; ethylene oxide – [C2H4O]; 1,2-dibromo-3-chloropropane (DBCP) – [C3H5Br2Cl]
    Developmental Toxicity
      Adverse effects manifested in the embryonic or fetal periods or postnatally, associated with exposure during pregnancy.
        e.g., ethylene oxide – [C2H4O]; thalidomide – [C13H10N2O4]

## Slide 17: Physiological Effects
Teratogens
  Agents that cause irreversible deleterious structural malformations in an embryo as a consequence of exposure of the mother during pregnancy.
    e.g., ethylene oxide – [C2H4O]; thalidomide – [C13H10N2O4]
Sensitization
  Agent that can cause an allergic response in susceptible individuals.
    e.g., methylene bisphenyl isocyanate (MDI) – [C15H10N2O2]; trichloroethylene – [C2HCl3]

## Slide 18: Hazard Classification
Hazard Communication Standard (HCS) 2012
1910.1200

## Slide 19: Reasons for Sampling

## Slide 20: Sampling Reasons
Characterization of contaminant(s) and/or condition(s) present in the work environment through identification and quantification.
Estimation of employee exposure
Assess compliance
Evaluation of the effectiveness of work place controls (i.e., engineering controls, PPE)

## Slide 21: Types of Sampling

## Slide 22: Types of Sampling
Integrated
  Averages concentration over long periods of time
    Can consist of one sample or multiple samples
  Known volume of air passed through a collection device to remove a specific contaminant(s)
  Used to determine TWA
    Typically, 15 minutes – 8 hours
Grab / Spot
  Environmental concentrations at a specific point in time
    Can analysis multiple contaminants
  Sampling collected over a short period of time
    Usually less than 5 minutes
  Can be used to estimate time-weighted average (TWA)

## Slide 23: Types of Sampling
Personal
  Breathing Zone
    TWA
      Full-shift
      Partial-shift
    Ceiling / Excursion / STEL
      Typically 15 minutes
    Variations
      Tasks performed
  Biological
    Biological exposure indices (BEIs)
      Full-shift
Area
  Specific area / fixed locations
    TWA
      Full-shift
      Partial-shift
    Ceiling / Excursion / Short Term Exposure Limit (STEL)
      Typically 15 minutes
    Variations
      Equipment
      Processes

## Slide 24: Types of Sampling
Active
  Physically/forcibly moving air.
    through media
    Into a collection device
    Across membranes
  TWA
    Area
    Personal
  Ceiling / Excursion / STEL
    Area
    Personal
Passive
  Passive diffusion
    Fick’s first law of diffusion
  TWA
    Area
    Personal
  Ceiling / Excursion / STEL
    Area
    Personal

## Slide 25: Types of Sampling
Screenings (Grab / Spot)
  Provide proof of the existence of the contaminant
    Wipe samples
      Establish presence of contaminant
      Can determine concentration within a defined area
        Difficult to interpret results
    Bulk samples
      Establish and identify contaminant
      Sometimes necessary to support analysis
    Direct read instruments
      Instantaneous
      Can provide quantification
      Can be used to determine TWA

## Slide 26: Full-shift Sampling
Defined to be a minimum of the total time of the shift minus 1 hour.
  e.g., 7 hours of an 8-hour work shift or 9 hours of a 10-hour work shift.
Make every attempt to sample as much of the work shift as possible, including segments of the greatest exposure.
FOM Chapter XV

## Slide 27: Full-shift Sampling
Monitoring may be accomplished with a full shift single sample or continuous multiple samples taken to determine any 8 hours of exposure for comparison with the permissible exposure level (PEL).
A separate sample should be used to determine any additional exposure beyond 8 hours.

## Slide 28: Partial-shift Sampling
Less than 7 hours of an 8-hour shift
  Professional judgment is necessary for making any conclusions or assumptions regarding the un-sampled period
    i.e. the set-up and/or take-down time which is not to exceed 1 hour.
  The CSHO should carefully document the rationale for any professional judgment regarding un-sampled exposure periods.
  A determination that any employer is in compliance will not be made in any case unless the sampled period is representative of the employee's normal exposure.

## Slide 29: Ceiling Sampling
Typically a 15 minute sample
Monitoring may be accomplished with a single sample to determine the exposure for comparison with the ceiling limits.
Select time period of greatest concern and potential for exposure.

## Slide 30: Biological Monitoring
Indirectly reflects the dose to a worker from exposure to the chemical of interest.
  Sampling time
    Prior to shift
    During shift
    End of shift
    End of the workweek
    Discretionary
  Examples
    Urine Analysis
    Blood Analysis
    Expired Breath Analysis

## Slide 31: Sampling Equipment

## Slide 32: Sampling for Gases and Vapors
Grab / Spot Sampling
  Evacuated Containers
  Displacement Collectors
  Flexible Plastic Bags
Integrated Sampling
  Absorbers
  Adsorption Media
  Flexible Plastic Bags

## Slide 33: Grab Sampling for Gases/Vapors
Evacuated Containers
  Flasks are heavy-walled containers of glass or other suitable material, where air has been removed, created a vacuum.
    Usually 200-1000ml in volume
    Open container
      Air is drawn in
    Seal flask
    Ship for analysis

## Slide 34: Sampling for Gases/Vapors
Flexible Plastic Bags
  Variety of sizes
  Common materials used for bags;
    Polyester
    Polyvinylidene chloride
    Teflon
    Fluorocarbons
  Air drawn into bag by hand pump or battery operated pump
  Can be used for either grab or integrated sampling

## Slide 35: Commonly used to collect
Evacuated containers
  e.g., oxygen – [O]; carbon dioxide – [CO2]; carbon monoxide – [CO]; nitrogen – [N]; methane – [CH4]
Flexible Plastic Bags
  e.g., organic and inorganic vapors and gases

## Slide 36: Integrated Sampling for Gas/Vapors
Absorbers
  Impinger
    Air is passed through liquid, the contaminant is captured by the liquid.
    Types
      Gas-wash
      Spiral absorbers
      Fritted bubblers

## Slide 37: Integrated Sampling for Gas/Vapors
Adsorption Media
  Solid-sorbent tubes
    Air is passed through the tube and binds to the media
    Types
      Activated charcoal based
        Most common
        Organic vapors
      Silica gel based
        Polar molecules
      Impregnated solid sorbent
        Specific contaminant

## Slide 38: Integrated Sampling for Gas/Vapors
Passive monitors
  Utilize Brownian motion to control the sampling process into a collection medium
    Follows Fick’s Law
  Very easy to use

## Slide 39: Commonly used to collect
Absorbers
  Impingers
    e.g., formaldehyde – [CH2O]; iodine – [I]
Adsorption Media
  Solid-sorbent tubes
    Activated charcoal based
      e.g., aliphatic, aromatic, halogenated hydrocarbons, alcohols, ethers, acetates, carbon disulfide – [CS2]
    Silica gel based
      e.g., Amines, acids, methanol – [CH3OH]
    Impregnated solid sorbent
      e.g., 1,3-Butadiene – [C4H6], ethylene oxide – [C2H4O]
  Passive monitors
    e.g., formaldehyde – [CH2O], mercury – [Hg],

## Slide 40: Sampling for Gases and Vapors
Direct-Reading Instruments
  Typically used to rapidly detect
    flammable or explosive atmospheres
    oxygen deficiency
    specific gases and vapors
      Typically Not designed to measure or detect below 1 ppm
      Only for specific classes of chemicals; or
      Only for one particular substance or chemical

## Slide 41: Sampling for Particulates
Grab / Spot Sampling
  Bulk
  Wipe
Integrated Sampling
  Filtration
  Impaction and Impingement
  Elutriation
  Centrifugal Collection
  Electrostatic Precipitation

## Slide 42: Sampling for Particulates
Bulk
  Physical collection of suspect material
    Necessary to support analysis of air samples and presence of hazard
  Collected in plastic bad, glass container, or plastic container.
  Commonly used to collect
    e.g., asbestos; combustible dust; silica – [SiO2]

## Slide 43: Sampling for Particulates
Wipe
  Wiping a predetermined area
    Establish presence of contaminant
      Can determine concentration within a defined area
        Difficult to interpret results
    Used to support effectiveness of PPE, housekeeping, and personal hygiene
  Commonly used to collect
    e.g., Lead – [Pb]; chromium (VI) – [Cr]; isocyanates

## Slide 44: Sampling for Particulates
Filtration
  Most common method
  Air passes through the filter, particles impact onto the filter
  Types
    Glass fiber
      e.g., oil mist
    Mixed Cellulose ester
      e.g., asbestos
    PVC
      e.g., chromium (VI) – [Cr]
    PTFE (Teflon) with XAD-2 tube
      e.g., coal tar pitch

## Slide 45: Sampling for Particulates
Impaction Impingement
  Cascade impactors
    Constructed with several stages to separate dust by size fractions
      Causing a sudden change in direction in airflow
        Particle’s momentum causes it to impact on the stage
    Collects viable or non-viable samples
    Commonly used to collect
      e.g., mold

## Slide 46: Sampling for Particulates
Impingement
  Impinger
    Air is passed through liquid, the contaminant is captured by the liquid.
    Commonly used to collect
      e.g., dust
    Not really used much anymore for collecting particulates

## Slide 47: Sampling for Particulates
Elutriation
  Used to remove unwanted materials and/or to remove larger size particles
  Types
    Vertical elutriator
      e.g., cotton dust
    Horizontal elutriator
      e.g., mineral dust

## Slide 48: Sampling for Particulates
Centrifugal Collection
  Used to determine the respirable fraction
  Air stream enters the device and through centripetal force, eliminates particles larger than 10 microns.
    Types
      Aluminum
      Nylon
    Commonly used to collect
      e.g., silica – [SiO2]

## Slide 49: Sampling for Particulates
Electrostatic Precipitation
  High airflow, where particulates pass through a high-voltage electrical field
    Particulates are attracted to the cylinder wall where they are collected
  Commonly used to collect
    e.g., nanoparticles, metal fumes

## Slide 50: Sampling for Particulates
Direct-Reading Instruments
  Typically used to rapidly detect
    Particulate size distribution
      Respirable dust
      Total dust
    Results are non-specific

## Slide 51: Sampling for Noise
Grab / Spot Sampling
  Sound level meters (SLMs)
  Octave Band Analyzer (OBA)
Integrated Sampling
  Noise Dosimeters

## Slide 52: Sampling for Noise
Sound level meters (SLM)
  Microphones change energy from sound waves to mechanical energy
    Types of Microphones
      Dynamic: mylar; vibrates with sound
      Ceramic: crystals; distorted by sound; sends out piezoelectric signal.
      Condenser: capacitor; measures voltage difference across gap (best type)
        Type II
          Intended for general field use
          Typically ± 2 dB

## Slide 53: Sampling for Noise
Sound level meters
  Measures
    Slow
      Averages the response out so the SLM can be read more easily
    Fast
      Used for intermittent noise (i.e., allows you to measure peaks)
    Impact
      Transient acoustical event less than half second in duration separated by greater than one second between peaks

## Slide 54: Sampling for Noise
Octave Band Analyzer
  Provides frequency analysis
    Useful to select the proper controls to reduce dB

## Slide 55: Sampling for Noise
Noise Dosimeters
  Measures noise levels and compares them to the 8-hour PEL and AL
  Read-out expressed as dose percentage.
  Settings used to determine dose percentage
    Criterion level – compared level (90 dB and 80 dB), read-out will be expressed as a percentage
    Threshold level – level below which noise will not be registered by the meter
    Exchange rate – amount of increase in sound pressure level that reduces the exposure time in half (e.g., OSHA uses 5 dB)

## Slide 56: Sampling for Heat
Grab / Spot Sampling
  Thermometers (temperature)
  Anemometers (air flow)
  Psychrometry (humidity)
  Wet-bulb, Globe, Thermometer (WBGT)

## Slide 57: Sampling for Ergo
Grab / Spot Sampling
  Camera
    Photographs
    Movies
  Spot watch
  Scale

## Slide 58: Sampling for Ergo - Vibration
Grab / Spot Sampling
  Accelerometers
    Common systems use a vibration transducer which transforms the mechanical motion into an electrical signal.

## Slide 59: Radiation
Ionizing vs non-ionizing
  Ionizing
    Alpha
    Beta
    Gamma
    Neutrons
  Non-ionizing
    Light
      Lasers
    Ultraviolet radiation
    Radiofrequency

## Slide 60: Sampling for Radiation
Ionizing
  Grab / Spot Sampling
    Geiger Counter
  Integrated Sampling
    Dosimeters
Non-Ionizing
  Grab / Spot Sampling
    Light Meter
    RF Meter

## Slide 61: Analytical Techniques

## Slide 62: Analysis Techniques
Gravimetric Techniques
  Most frequently used
  Calculate based on weight gain
Titrimetric Methods
  Using a known concentration to determine an unknown concentration volumetrically
    Acid-base
    Oxidation-reduction
Optical Methods
  Use of a microscope to count particles and fibers
Colorimetric Procedures
  Change of color intensity or tone

## Slide 63: Analysis Techniques
Spectrophotometric Methods
  Use infrared radiation spectra to the ultraviolet, measuring fractions transmitted or scattered
Spectrographic Techniques
  Vaporize sample, disperse it and photograph resulting spectrum for analysis
Chromatographic Methods
  Quantified by run times, when sample is passed through columns
Atomic Absorption Spectrophotometry
  Measures adsorption of radiation to determine concentration

## Slide 64: Sampling Strategy

## Slide 65: Methods of sampling
There are multiple types of sampling methods and the method(s) selected comes from professional judgement and evaluation being conducted.
  Time-weighted average (TWA)
    Determining exposure during the entire shift
      Typically 8 hours
  Ceiling/excursion limits/shot term exposure limits
    Determining short term exposures
      Typically 15 minutes
  Screenings
    Provide the existence of the contaminant
      Can provide quantification

## Slide 66: Sampling Strategy
General Considerations
  Preliminary Survey
  Worst case vs Typical day
  Whom/where/when to sample
  Analytical Method
  Sampling Equipment
  Sampling Necessary?

## Slide 67: General Considerations
Preliminary Survey
  Materials used/present
  Employee complaints or symptoms
  Process operations
  Workplace observations

## Slide 68: Materials/Products
Identify the raw material/products being used in production
  Review SDS/MSDS
  Review purchasing records
  Determine the chemical composition of the product(s)
    Do chemicals pose or potentially pose a hazard?
  Determination amount of raw material/products
  Identify any by-products produced during the production
    e.g., dust, carbon monoxide – [CO]

## Slide 69: Symptoms/Complaints
Documentation
  OSHA 300 logs
  Form 19s
  Medical Records
  Workers Compensation Claims
    Form WC-14
Interviews
  Management
    Employee complaints
    Sick employees
  Employees
    Experience any symptoms
      Co-workers
    Illnesses
    Concerns/Issues

## Slide 70: Process/Operation
Become familiar with the entire process operation.
  Start to finish
  Describe how raw materials/products are transformed into the sales/final product.
Identify equipment used
  Identify engineering controls in place.
Identify specific tasks/operational procedures
  Identify any task/operational hazards
    Noise
    Repetitive tasks
    Air contaminants

## Slide 71: Process/Operation
There are many processes and operations within the working environment that could expose employees to concentrations above the action level or permissible exposure limit.
  Examples
Welding | Dipping
Soldering | Plating
Painting | Mixing
Etching | Milling
Spraying | Drilling

## Slide 72: Workplace observation
PPE
  Respirators
    Dust Masks vs Full Face
Ventilation
  Mechanical vs Natural
Habits
Workplace Conditions
  Temperature
    Hot / cold
  Water damage
    Mold
  Visible contamination
    Dust clouds
    Fumes
    Dust piles
    Fog

## Slide 73: Worst Case vs Typical Day
  Worst case
    Representative of the highest potential exposures during process operations
  Typical Day
    Representative of normal process operations
Goal for compliance is to sample worst case.

## Slide 74: Whom/Where/When
Where
  Sample location
    Operation
    Department
  Sampling
    Area
      Workplace
      Specific operation
    Personal
      Breathing zone

## Slide 75: Whom/Where/When
Whom
  Select the maximum risk employee(s)
  Employee(s) location to operation/area
  Employees who perform similar tasks
When
  Differences between shifts
  Ventilation changes
  Weather conditions
  Process change(s)
  Unusual situation(s)
  Worst case scenario(s)
  Specific task(s)

## Slide 76: Sample Analysis
Sample Analysis
  Accreditation
    Analytics
    OSHA’s Salt Lake Technical Center (SLTC)
Analytical Methods
  Validation
    OSHA method or NIOSH method
      Few exceptions
  Interferences
    Positive
      Gravimetric analysis
    Negative
      Depletion of contaminant
    Combustible Dust
      Moisture

## Slide 77: Sampling Strategy
8-hours TWA
  Full period single sample
  Full period consecutive samples
  Partial period consecutive samples
  Grab samples measurement(s)
Ceiling
  Full period single sample
  Grab samples measurement(s)

## Slide 78: Considerations
Sample Duration
  TWA vs Ceiling
    Check Method for minimum/maximum sample volume and flow rates
  Calculate minimum sample time
  Example
    NIOSH 7300 – Lead
      Minimum sample volume = 50 L
      Maximum sample volume = 2000 L
      Flow rate 1 to 4 L/min
        Minimum sample time = 50 to 12.5 minutes
Tech Man: Sec II Ch 1

## Slide 79: Considerations
Media
  Availability
  Overnight shipping
Number of Samples
  Includes field blanks
Cost
  Method
  Media

## Slide 80: Analytics - Book

## Slide 81: Sampling Equipment
Good working order
Availability
  Plus additional back ups
Charged

## Slide 82: Sampling Necessary?
Potential exposure?
Related symptoms present?
Contaminant / Condition present?
Employer’s exposure assessment?
Previous sampling conducted by NCDOL?

## Slide 83: Sampling Necessary?
Employer’s exposure assessment
  Who conducted the sampling?
    Credentials?
    Third-party?
  Sampling Method Used?
  Sample Time?
  Employee(s) Sampled?
    Representative?
  Operation(s)
  Number of samples?
  Meets requirements of standard where applicable?
    e.g., ethylene oxide – [C2H4O]

## Slide 84: Sampling Necessary?
OSHA’s additional monitoring requirement
  Whenever there has been a change in the production, process, control equipment, personal or work practices that may result in new or additional exposures or when the employer has any reason to suspect that a change may result in new or additional exposures.

## Slide 85: Includes Personal
  DBCP
    1910.1044(f)(4)
    1926.1144
  Acrylonitrile
    1910.1045(e)(4)
    1910.1145
  Ethylene Oxide
    1910.1047(d)(5)
    19126.147
  MDA
    1910.1050(e)(5)
    1926.60(f)(5)
  1,3-Butadiene
    1910.1051(d)(5)(i)
  Silica
    1910.1053(d)(4)
    1926.1153(d)(2)(iv)
  Asbestos
    1910.1001(d)(5)
    1926.1101(f)(4)(ii)
  Inorganic Arsenic
    1910.1018(e)(4)
    1926.1118
  Beryllium
    1910.1024(d)(4)
    1926.1124(d)(4)
  Lead
    1910.1025(d)(7)
    1926.62(d)(7)
  Chromium (VI)
    1910.1026(d)(2)(vi)
    1910.1126(d)(2)(vi)
  Cadmium
    1910.1027(d)(4)
    1910.1126(d)(4)

## Slide 86: Differences
Unique
  Formaldehyde
    1910.1048
    1926.1148
  13 Carcinogens
    1910.1003 – 1910.1016
    1926.1103 – 1926.1116
Doesn’t include personal
  Vinyl Chloride
    1910.1017(d)(3)
    1926.1117
  Coke Oven Emissions
    1910.1029(e)(2)
    1926.1129
  Cotton Dust
    1910.1043(d)(3)(iii)
  Methylene Chloride
    1910.1052(d)(4)(i)
    1926.1152

## Slide 87: NCDOL Sampling

## Slide 88: NCDOL Sampling
  The scope of the sampling episode was limited to the activity in the work environment on the day of sampling. Although an effort was made to ensure sampling was conducted on a typical workday, the sampling data may not be representative of exposures on subsequent workdays due to changes in production, work practices, equipment, or other factors.
  The data should not be used to predict exposures in the future in lieu of collection of additional monitoring data to determine compliance after changes are made to the work environment.

## Slide 89: Sampling Necessary?
FOM Chapter – XV.C.2.
  Sampling procedures should be conducted for all complaints and referrals alleging exposure to substances.
  If the CSHO determines that sampling is not necessary, the CSHO will discuss this with their supervisor.
  If sampling is not conducted, the CSHO will document the reasons in the case file.

## Slide 90: Sample Collection
Air and Noise Samples

## Slide 91: Calibration Worksheet
NCDOL Photo Library

## Slide 92: Calibration
Sampling equipment checked out, inspected and calibrated before use (on-site if possible).
  Pre and Post calibration must be recorded on the Calibration Worksheet for each piece of sampling equipment.

## Slide 93: Field Sampling Worksheet
NCDOL Photo Library
NCDOL Photo Library

## Slide 94: Day of Sampling
Field Sampling Worksheet

## Slide 95: Day of Sampling
Field Sampling Worksheet

## Slide 96: Day of Sampling
Field Sampling Worksheet

## Slide 97: Day of Sampling
Field Sampling Worksheet

## Slide 98: Breaks and Sampling
Lunch breaks
  Not advisable to sample during lunch breaks
    Employee may leave the company premises
    Unless employees eat in areas where potential exposure exists.
Bathroom breaks
  Not advisable to sample during bathroom breaks.
    Depends on the sampling equipment (e.g., Edge 5s)
Regular breaks
  Continue to sample during regular breaks.
    Unless employees leave the company premises
    Unless employees go for a smoke break

## Slide 99: Breaks and Sampling
Removal of equipment
  Turn off device prior to break and turn on again after returning from break.
  Care taken to assure that contamination of collection medium does not occur.
    Ensure sample media and equipment go back on the same person.
  The time it is off should not be counted as sample time for calculation of TWA.

## Slide 100: Day of Sampling – Equipment Checks
Field Sampling Worksheet

## Slide 101: Equipment Checks
Once sampling equipment is placed on employee or area
  Check on sampling equipment
    First 30 minutes
    1-hour after the 30 minutes
    2 hours after the first hour
CSHO must remain at workplace while samples are being collected.
FOM XV.C.2.c

## Slide 102: Observation
Observe employee(s) during sampling
  Note any deviation(s) from procedure
    Non-routine tasks
    Additional protections
      New engineering controls
      Rotation
      PPE usage
    Shorten duration
  Anything else of importance

## Slide 103: Day of Sampling - Observation
Field Sampling Worksheet
Record any and all observations here

## Slide 104: After Sample Collection
Post Calibrate sampling equipment, immediately after sampling.
  Document on Calibration Worksheet for each piece of sampling equipment.
Difference between pre and post flow rates as a general rule should not be greater than 5%

## Slide 105: Example 1
Not calibrated on-site
Not immediately post calibrated

## Slide 106: Example 2

## Slide 107: Analytics Lab Test Request Form
Photo Source: NCDOL Photo Library

## Slide 108: Calculating Sample Volume
  Example
    Sampled at a flow rate of 1.7 L/min
    Sample for 7 hours (420 minutes)

## Slide 109: Calculating Sample Volume
What is the sampling flow rate and sample volume for Example 2?
Pre-cal = 50.571 mL/min
Post-cal = 48.501 mL/min
Average of pre and post = 49.536 mL/min
Pre-Calibration | Post-Calibration
50.571 mL/min | 48.501 mL/min

## Slide 110: Answer
Pre-cal = 50.571 mL/min
Post-cal = 48.501 mL/min
Average = 49.536 mL/min

## Slide 111: Reason
Example – PEL 1ppm
  43µg was detected on one sample collected over 480 minutes.
    Typical reports
      mg/m3 and/or ppm
      43µg = 0.043mg
Pre-cal = 50.571 mL/min
Post-cal = 48.501 mL/min
Average of pre and post = 49.536 mL/min

## Slide 112: Conversions
Pre-cal
50.571 mL/min x 480 min = 24274.08 mL
24274.08 ml = 24.27408 L = 0.02427408 m3
Post-cal
48.501 mL/min x 480 min = 23280.48 mL
23280.48 mL = 23.28048 L = 0.02328048 m3
Average
49.536 mL/min x 480 min = 23777.28 mL
23777.28 mL = 23.77728 L = 0.02377728 m3

## Slide 113: Concentrations
Pre-Cal
0.043mg / 0.02427408 m3 = 1.77 mg/m3
1.77 mg/m3 = 0.98 ppm
Post-Cal
0.043mg / 0.02328078 m3 = 1.85 mg/m3
1.85 mg/m3 = 1.03 ppm
Average
0.043mg / 0.02377728 m3 = 1.81 mg/m3
1.81 mg/m3 = 1.00 ppm

## Slide 114: Form 21 Tape

## Slide 115: Form 21 Tape

## Slide 116: Form 21 Tape

## Slide 117: Sample Collection
Wipe Samples

## Slide 118: Wipe Sampling
Wipe Sampling Procedures
  FOM Chapter XV
    Refer to the OSHA Technical Manual
Prior determination of wipe sample locations
  Surfaces
    e.g., Floor, desks, tables, door knobs, etc.
  Employees’ skin
    e.g., hands, face.
Each wipe sample
  A new set of clean, disposable, powder-free gloves must be used for each sample.
    prevents false positives

## Slide 119: Day of Sampling
Record each location with a unique identifier.
  Photograph each location and specify each location within the facility.
    If photographs cannot be taken, sketches, diagrams, and other means of identifying locations are acceptable.
Don gloves
Remove media (e.g., filter) from packaging / cassette / vial with tweezers or fingers.
  If a damp wipe sample is desired, moisten the filter with distilled water or other solvent as recommended.
    Note: For skin sampling use only distilled water.

## Slide 120: Day of Sampling
Place single-use 10cm x 10cm templates at desired location
Using the media, wipe an area about 100 cm2, rubbing the entire area side to side, then up and down.
  When wiping, apply firm pressure
  In many cases (such as knobs and levers) it may not be possible to wipe 100 cm2.
    Sample cannot be quantified
Place media in a sample vial, cap and label it with the same unique identifier as the location.

## Slide 121: Day of Sampling
Remove and dispose gloves.
Include additional relevant details regarding the nature of the sample
  e.g., inside Fred’s respirator, “x” distance from contaminant generating process
At least one blank media treated in the same fashion, but without wiping, should be submitted for each sampled area.

## Slide 122: Day of Sampling
Some substances (e.g., benzidine, hexavalent chromium, and 4,4’-methylenedianiline) are unstable and may require a solution to be added to the vial as soon as the wipe sample is placed in the vial or may require other special sample handling.

## Slide 123: After Sampling Collection
Submit the samples, each sealed with a Form OSHA-21, and in accordance with any special procedures located in OTM Section II Chapter 4 (Sample Shipping and Handling).

## Slide 124: Sample Collection
Bulk Samples

## Slide 125: Bulk Sampling
Bulk Sampling Procedures
  FOM Chapter XV
    Refer to the OSHA Technical Manual
Locations
  Prior determination after walk-around
  Immediate during walk-around
Equipment
  Plastic container, natural bristle brush and non-sparking dust pans
    e.g., combustible dust
  Plastic bag and gloves
    e.g., paint chips

## Slide 126: Dust – Day of Sampling
Each type of dust must be collected as a separate sample
  Collect at least 1 liter of dust per sample
  If grain dust collect two samples
Suggested locations
  “High spaces” such as roof beams, open web beams, and other ceiling supports; tops of pipes, railing, ductwork, conduit, electrical boxes/panels and other horizontal surfaces located as high in the overhead as possible.
    Samples from floor level present a significantly reduced potential for dust cloud generation

## Slide 127: Dust – Day of Sampling
Record each location where sample was collected.
  Document each location within the facility.
    Do not take photographs
    Use sketches, diagrams, and other means of identifying locations were samples were taken from.
  Document where, when, and how dust is used and/or generated.
Don gloves
Use natural bristle hand brush to sweep accumulated dust into non-sparking dust pans.

## Slide 128: Dust – Day of Sampling
Transfer dust from dust pans to plastic container.
Upon completion
  Affix an OSHA-21 sample identification seal to the container.
    To seal the container, apply one end of the seal to the center of the lid, and run the seal down the edge of the lid and as far down the side of the container as it will reach
  Complete the Receipt of Evidence or Property Form
  If available collect MSDS/SDS of dust or raw materials

## Slide 129: Receipt of Evidence/Property Form

## Slide 130: Dust – Day of Sampling
Storage
  Secure sample(s)
Approval must be received prior to sending sample for analysis
  Typically after file is contested
Fill out form 91 to submit to SLTC
  Must specify test to be done
    Request “Potential Class II Dust” to support electrical violations
      e.g., 29 CFR 1910.307
    Request “Kst” to support fire or explosion hazards that may result from housekeeping or 95-129(1).

## Slide 131: Dust - Submission

## Slide 132: Evaluation of Sampling Results
Air and Noise Samples

## Slide 133: Understanding Results
Direct Reading Results
  Directly displayed on screen
  Print outs
In-House Results
  Equipment software
    Print outs
Laboratory Results
  Mailed results
    Amount detected

## Slide 134: Direct Print Out – Sound Results: Edge 5s

## Slide 135: Direct Print Out – Sound Results: Edge 5s

## Slide 136: Direct Print Out – Sound Results: Edge 5s
Threshold – 80 dB(A)
  AL 85 dB(A)
    TWA – 95.7 dB
      Projected – 95.9 dB
    Dose – 220.7%
      Projected – 228.8%
    Lavg – 95.9 dB
    Peak – 104.8 dB
Threshold – 90 dB(A)
  PEL 90 dB(A)
    TWA – 95.4 dB
      Projected – 95.6 dB
    Dose – 212.4%
      Projected – 220.2%
    Lavg – 95.6 dB
    Peak – 104.8 dB

## Slide 137: Noise Equations
Dose
  C is the total time of exposure at specific noise level
  T is reference duration for noise exposure
  %D is percentage dose

## Slide 138: Dose Example
Calculate the dose for an employee who is exposed to the follow noise levels:
  95 dB(A) for 1 hour
  90 dB(A) for 3 hours
  105 dB(A) for 10 minutes
  93 dB(A) for 2 hours
  86 dB(A) for 1 hour
  Answer:

## Slide 139: Noise Equations
TWA
  %D is percentage dose

## Slide 140: TWA Noise Example
Calculate the TWA in dB(A) for an employee was exposed to noise at a dose of 140.7%
  Answer:

## Slide 141: Noise Equations
Distance
  SPL is sound pressure level in dB(A)
  d is distance in feet or meters

## Slide 142: Distance Noise Example
You measure the sound pressure level of 95 dB(A) from 5 feet away from the noise source, what is the sound pressure level the employee is exposed to at 1 foot away?
  Answer:

## Slide 143: Laboratory Results

## Slide 144: Sample Break-Through
Sample break-through
  If the back-up section of the sampling media contains >25% of the contaminant then the sample should be considered invalid.

## Slide 145: Equations
Calculation of potential exposure concentrations
However, no more than eight hours of sampling can be used in the 8-hour TWA calculation

## Slide 146: Equations
A zero exposure will be assumed unless the CSHO can defend a professional judgment on the magnitude of the exposure for the unsampled period. Thus, a TWA should generally be calculated by dividing the sample results by 8 hours (or 480 minutes) rather than the actual time sampled

## Slide 147: TWA Equations
Actual
8-hour
  C is concentration
  T is actual duration of time sampled

## Slide 148: TWA Example 1
Sampling for Sulfuric Acid.
  PEL is 1 mg/m3
  Take one sample
    The sampling pump ran for 7 hours or 420 minutes.
  The laboratory reported a concentration of 1.1 mg/m3.
    8-hour TWA
Notes: So lets walk through an example of a TWA calculation using hypothetical numbers. In this example we only collected one sample.
  Actual TWA 𝑇𝑊𝐴= ((1.1 𝑚𝑔∕〖𝑚^3 𝑥 7 ℎ𝑜𝑢𝑟𝑠〗) )/(7 ℎ𝑜𝑢𝑟𝑠)
  8-hour TWA 𝑇𝑊𝐴= ((1.1 𝑚𝑔∕〖𝑚^3 𝑥 7 ℎ𝑜𝑢𝑟𝑠〗) + (0 𝑚𝑔∕〖𝑚^3 𝑥 1 ℎ𝑜𝑢𝑟)〗)/(8 ℎ𝑜𝑢𝑟𝑠)

## Slide 149: TWA Example 2
Sampling for Sulfuric Acid.
  Take two samples
    Sample 1
      The sampling pump ran for 4 hours or 240 minutes.
      The laboratory reported a concentration of 1.12 mg/m3 .
    Sample 2
      The sampling pump ran for 4 hours or 240 minutes.
      The laboratory reported a concentration of 1.13 mg/m3
        Actual & 8-hour TWA
Notes: Now lets walk through another example of a TWA calculation using hypothetical numbers, but this time we collected two samples.
  𝑇𝑊𝐴= ((1.12 𝑚𝑔∕〖𝑚^3 𝑥 4 ℎ𝑜𝑢𝑟𝑠〗)+(1. 13 𝑚𝑔∕〖𝑚^3 𝑥 4 ℎ𝑜𝑢𝑟𝑠)〗)/(8 ℎ𝑜𝑢𝑟𝑠)

## Slide 150: Sulfuric Acid Sampling
Example 2
  2 samples taken
    8 hours sampled
    Actual & 8-hour TWA
      1.125 mg/m3
Example 1
  1 sample taken
    7 hours sampled
    8-hour TWA
      0.9625 mg/m3
    Actual TWA
      1.1 mg/m3

## Slide 151: Equations
Severity / hazard ratio
  Y is the severity or hazard ratio
  C is the concentration or employee exposure
  OEL is the Occupational Exposure Limit

## Slide 152: Severity / Hazard Ratio
Example 2
  8-hour TWA
    1.125 mg/m3
    112.5% of the PEL
Example 1
  8-hour TWA
    0.9625 mg/m3
    96.25% of the PEL

## Slide 153: TWA Mixture Equation
For substances with occupational exposure limits (OELs) established for similar toxicological pathways and target organs.
  Compare results to unity (1)
    < 1 – below combined OEL
    > 1 – exceeds combined OEL
  C is 8-hour TWA concentration
  OEL is Occupational Exposure Limit

## Slide 154: Mixture Example
Sampling conducted
  carbon tetrachloride
    Sample 1 reported 2.9 ppm collected over 4 hours
    Sample 2 reported 3.5 ppm collected over 4 hours
      PEL is 10 ppm
  trichloroethylene
    Sample 1 reported 30 ppm collected over 4 hours
    Sample 2 reported 60 ppm collected over 4 hours
      PEL is 100 ppm
  vinyl chloride
    Sample 1 reported 0.39 ppm collected over 4 hours
    Sample 2 reported 0.23 ppm collected over 4 hours
      PEL is 1 ppm

## Slide 155: Mixture Example
carbon tetrachloride
  TWA is 3.2 ppm
trichloroethylene
  TWA is 45 ppm
vinyl chloride
  TWA is 0.31 ppm
Now we can do the mixture equation (Em)
  > 1, exceeds

## Slide 156: Statistical Analysis

## Slide 157: Accuracy of air sampling
Air sampling accuracy is ± 25% of the true value (given the errors during calibration, sampling, and analytical methods).

## Slide 158: Statistical Equations
Sampling and Analytical Error (SAE)
    1.645 is a statistical constant
    SrT is the Overall Precision
OSHA Methods: SAE can be read directly
NIOSH Methods: Must be calculated
Not listed: Contact the laboratory to get the SAE

## Slide 159: Statistical Equations
Confidence Limits: Full-Period, Single Sample
  Upper Confidence Limit (UCL)
  Lower Confidence Limit (LCL)
  Y is severity / hazard ratio.
  SAE is sampling and analytical error.
If LCL is ≥ 1, then a violation exists with a 95% confidence

## Slide 160: TWA Examples
Sampling for Sulfuric Acid.
  NIOSH Method 7903
    The SrT is 0.087
Sampling and Analytical Error

## Slide 161: TWA Example 1
Example 2
  Lower Confidence Limit (LCL)
  Upper Confidence Limit (UCL)
  LCL95% < 1 & UCL95% > 1
    the results are in the possible overexposure region.
Example 1
  Lower Confidence Limit (LCL)
  Upper Confidence Limit (UCL)
  LCL95% < 1 & UCL95% > 1
    the results are in the possible overexposure region.
Notes: Example 1
𝐿𝐶𝐿=0.9625−0.143115
𝑈𝐶𝐿=0.9625+0.143115
This shows that there is a possibility of an overexposure. The questions you want to ask as a CSHO, is this sample representative? If I would have sampled for 8-hours would I have an overexposure?
Concerns?
  Is this sample representative?
  Was this sample a worst case?
Example 2
Since this shows a possible overexposure according to the FOM, which then dictates for consecutive full-period sampling CSHO must use the equation on the next slide.

## Slide 162: Statistical Equations
Confidence Limits: Full-Period, Consecutive Sampling
  Upper Confidence Limit (UCL)
  Lower Confidence Limit (LCL)
  Y is severity / hazard ratio
  SAE is sampling and analytical error
  T is actual duration of time sampled
  X is concentration

## Slide 163: TWA Example 2
Calculated
  TWA = 1.125 mg/m3
  Severity / hazard ratio = 1.125
Lower Confidence Limit (LCL)

## Slide 164: Statistical Equation
Confidence Limits: Mixtures
  CL is mixture control limit
  Em is the equivalent exposure for the mixture
  Y is the exposure ratio
  R is the ratio to total exposure
  SAE is the sampling and analytical error
If Em > 1 and Em > CL = an overexposure

## Slide 165: Mixture Example
TWA
  carbon tetrachloride
  trichloroethylene
  vinyl chloride

## Slide 166: Mixture Example
  carbon tetrachloride
  trichloroethylene
  vinyl chloride

## Slide 167: Mixture Example
Ratio to total exposure
  carbon tetrachloride
  trichloroethylene
  vinyl chloride

## Slide 168: Mixture Example
  carbon tetrachloride
  trichloroethylene
  vinyl chloride
    1

## Slide 169: Mixture Example
Total Ratio
Mixture Control limit
Em = 1.08
CL = 1.077
Em > 1 & Em > CL.
  Therefore, an violation has been established.

## Slide 170: Equations
Field Sampling Worksheet
Recorded observations
Recommended to include your calculations in this area as well
  TWA
  Severity

## Slide 171: Evaluation of Sampling Results
Wipe Samples

## Slide 172: Wipe Results
OSHA does not have standards setting limits for surface contamination.
  Standard with housekeeping sections
    Inorganic arsenic – §1910.1018
    Beryllium – §1910.1024
    Lead – §1910.1025 & §1926.62
    Chromium (VI) – §1910.1026 & §1926.1126
    Cadmium – §1910.1027 & §1926.1127
    Etc.
      All use that same language “as free as practicable”.

## Slide 173: Wipe Results

## Slide 174: Understanding Wipe Results
Lead Wipe
  Concentration
    0.0273 µg/cm2
Does this concentration constitute a violation of the standard?

## Slide 175: Evaluation of Sampling Results
Bulk Samples

## Slide 176: Bulk Sample - Identification

## Slide 177: Bulk Sample - Dust Results

## Slide 178: Understanding Results
Reports may contain the following:
  Percent through 40 mesh
  Percent moisture content
  Percent combustible material
  Percent combustible dust
  Metal dusts will include resistivity
  Minimum explosive concentration (MEC)
  Minimum ignition energy (MIE)
  Class II test
  Sample weight
  Maximum normalized rate of pressure rise (dP/dt) – Kst Test
  Minimum ignition temperature

## Slide 179: Understanding Results

## Slide 180: Understanding Results
Kst
  The maximum rate of pressure rise generated when dust is tested in a confined enclosure.
Dust Explosion Class | Kst (bar.m/s) | Characteristic
St 0 | 0 | No Explosion
St 1 | >0 and ≤200 | Weak explosion
St 2 | >200 and ≤300 | Strong explosion
St 3 | >300 | Very strong explosion

## Slide 181: Understanding Results
Moisture
  Moisture in dust particles raises the ignition temperature of the dust because of the heat absorbed during heating and vaporization of the moisture.
    Ignition temperature of cornstarch may increase as must as 122F, with an increase of moisture content from 1.6% to 12.5%.
  The moisture in the air surrounding a dust particle has no significant effect on the course of deflagration once ignition has occurred.
    In order for moisture to prevent ignition of dust by common source, the dust would have to be so damp that a cloud could not be formed

## Slide 182: Recording Sampling Data
Air and Noise Samples

## Slide 183: Recording Sampling Data
All sampling data must be recorded
  OE
  Field Sampling Worksheet

## Slide 184
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 185: Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 186
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 187
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 188
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 189
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 190
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 191
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 192
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 193
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 194
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 195
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 196
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 197
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 198
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 199
Entering Sampling Data in OE
Photo Source: NCDOL Photo Library

## Slide 200
Entering Noise Results
Photo Source: NCDOL Photo Library

## Slide 201
Entering Noise Results
Photo Source: NCDOL Photo Library

## Slide 202
Entering Noise Results
Photo Source: NCDOL Photo Library

## Slide 203
Entering Noise Results
Photo Source: NCDOL Photo Library

## Slide 204
Entering Noise Results
Photo Source: NCDOL Photo Library

## Slide 205
Entering Noise Results
Photo Source: NCDOL Photo Library

## Slide 206
Entering Noise Results
Photo Source: NCDOL Photo Library

## Slide 207: Entering Results
Field Sampling Worksheet
  All sampling data must be record
Noise AL
Noise PEL
8111
8110
0560
Carbon Monoxide
TWA
TWA
TWA
49
97
5
%
%
PPM
50
100
50
0.98
0.97
0.10
No
No
No
Yes
Yes
Yes
Your Signature

## Slide 208: Recording Sampling Data
Bulk and Wipe Samples

## Slide 209: Entering Bulk & Wipe Data

## Slide 210: Entering Bulk Data

## Slide 211: Entering Bulk Data

## Slide 212: Enter Wipe Data

## Slide 213: Enter Wipe Data

## Slide 214: Recording Sampling Data
Direct Read Samples

## Slide 215: Entering Direct Read Data

## Slide 216: Entering Direct Read Data

## Slide 217: Entering Direct Read Data

## Slide 218: Entering Direct Read Data

## Slide 219: Entering Direct Read Data

## Slide 220: Entering Direct Read Data

## Slide 221: Entering Direct Read Data

## Slide 222: Entering Direct Read Data

## Slide 223: Recording Sampling Data
Screening Samples

## Slide 224: Entering Screening Data

## Slide 225: Entering Screening Data

## Slide 226: Entering Screening Data

## Slide 227: Entering Screening Data

## Slide 228: Carbon Monoxide
OPN 148

## Slide 229: OPN-148
For situations where significant exposure(s) to CO occurred, resulting in medical intervention and/or hospitalization.
Theoretically derive an employee’s exposure to CO
  Coburn Equation
  Coburn-Forster-Kane Model

## Slide 230: OPN-148
Must request medical records of suspected employees.
  % carboxyhemoglobin (COHb or HbCO)
Smoker or non-smoker
Assess individual’s physical activity level for assigned job task(s).
Description of work activity for assigned job task(s).
Determine the entire time period (in minutes) to which the individual(s) were occupational exposed to CO.
Appendix B

## Slide 231: Con’t
Determine time period between the end of CO exposure and blood sample taken (in minutes).
Recovery Time (air, oxygen, hyperbaric or mixture)
  Mixture
    Include time for each type of treatment
Appendix B

## Slide 232: Coburn Equation
CO = theoretical concentration of CO in air (ppm)
C = Blood COHb in % at the time of blood sample
B = Activity Factor (sedentary = 0.152, light work = 0.065, heavy work = 0.040)
D = background COHb level (non-smoker = 0.0015, smoker = 0.0100)
t = time of exposure to CO (in minutes)
𝜃 = time between end of CO exposure and blood sampling (in minutes)
T = half-life recovery factor of CO removal from blood (in minutes)

## Slide 233: Coburn Equation
FIS
  Forms
    10 Forms COB 1: Coburn Equation CO Calculator

## Slide 234: Reference
OSHA
  CO PEL = 50 ppm
NIOSH
  CO REL = 35 ppm
  Ceiling = 200 ppm
ACGIH (2014)
  CO TLV = 25 ppm
  CO BEI
    Blood (end of shift) = 3.5% of hemoglobin
    Exhaled air (end of shift) = 20 ppm

## Slide 235: Example 1
Employee #1
  COHb % at time of blood sample = 4.5%
  Activity Factor = Sedentary
  Background COHb = non-smoker
  Exposure time to CO = 8 hours
  Time between end of CO exposure and collection of blood sample = 1 hour
  Recovery method = Air

## Slide 236: Example 2
Employee #1
  COHb % at time of blood sample = 6.5%
  Activity Factor = Heavy Work
  Background COHb = Smoker
  Exposure time to CO = 30 minutes
  Time between end of CO exposure and collection of blood sample = 45 minutes
  Recovery method = Mixture
    Air recovery time = 15 minutes
    Oxygen recovery time = 30 minutes

## Slide 237: Carbon Monoxide
OPN 148
  If Coburn Equation results in > 50 ppm
    Get supervisor’s approval to initiate the Coburn-Forster-Kane Model.
      Done by Salt Lake Technical Center (SLTC)
      Model has been extensively tested for reliability.
  Download SLTC Application
    Directions in Appendix C
    Requires a OSHA Extranet account

## Slide 238: SLTC Application

## Slide 239: SLTC Application
Detailed questions
  25 numbered questions
  Any sampling information taking during event (e.g., emergency responders)
  Symptoms or signs employees exhibited.
  Refer to the catalog of activity levels
Recommendation
  Download this form prior to conducting inspection to ensure the gathering of all necessary information.

## Slide 240: Common Citations

## Slide 241: Noise Citations
When the 8-hour TWA is ≥ 92 dB(A) (a dose of 132%)
  Exceeds the permissible noise exposure
    Cite 29 CFR 1910.95(b)(1) or 29 CFR 1926.52(b)
      Serious
        Hearing protection not provided or properly utilized; and/or
        Hearing conservation program is deficient or nonexistent
      Non-Serious
        Effective hearing protection provided and utilized; and
        Hearing conservation program is effective
        Employer has an effective training program.

## Slide 242: Noise Citations
When the 8-hour TWA is ≥ 87 dB(A) (a dose of 66%)
  Cite for Hearing Conservation Program if non-existent
    29 CFR 1910.95(c)(1) or 29 CFR 1926.52(d)(1)
        Serious
          8-hour TWA ≥ 92 dB(A) (a dose of 132%)
        Non-Serious
          8-hours TWA ≥ 87 dB(A) but < 92 dB(A)

## Slide 243: Air Contaminant Citations
Limits for air contaminants are exceeded
  Air contaminant concentration ≥ acceptable levels
    Table Z-1
      Cite 29 CFR 1910.1000(a)(1) or (2)
    Table Z-2
      Cite 29 CFR 1910.1000(b)(1) or (2)
    Table Z-3
      Cite 29 CFR 1910.1000(c)
    Threshold Limit Values of Airborne Contaminants for Construction
      Cite 29 CFR 1926.55(a)
    Lack of engineering controls and/or administrative and work practice controls
      Cite 29 CFR 1910.1000(e) or 29 CFR 1926.55(b)
FOM ch XV F.4.d-e

## Slide 244: General Duty Clause §95-129(1)
Substance with no OSHA PEL
  If the substance’s dose (exposure) and toxicity could result in a serious illness or injury; and
  The substance has an OEL set by other entities
    TLV published by ACGIH
    REL recommendation by NIOSH
      10 hour TWA
  Exceptions (further discussion needed with supervisor and bureau chief)
    Substance concentration below established PEL, but in excess of a TLV or REL
    Substance has a PEL with no established ceiling limit, but a ceiling from either ACGIH or NIOSH

## Slide 245: General Duty Clause §95-129(1)
Heat Stress
  OPN 141 – Enforcement Guidance for Conducting Heat-Related Illness Inspections and Issuing Citations
Ergonomics
  FOM Chapter 17 – Ergonomics Inspection Procedures
Combustible Dust
  NEP: Combustible Dust Explosion Prevention Program

## Slide 246: Air Contaminant Citations
Grouping
  Situations where an overexposure is documented, feasible engineering and/or administrative controls have not been implemented, and respiratory protection has not been provided or is insufficient or ineffective
    Overexposure for regulated contaminants
      29 CFR 1910.1000(a), (b), (c), (d) or 29 CFR 1926.55(a)
    Engineering/administrative controls
      29 CFR 1910.1000(e) or 29 CFR 1926.55(b)
    Respirator
      29 CFR 1910.134(a)(2)

## Slide 247: Citation Classification
Guidance
  Based on Health Codes from the Chemical Sampling Information page on the OSHA website
    Substances with a health code of 13 or less
      Serious
    Substances with a health code of 6, 8, and 12
      Non-serious
        mild to temporary effects
    Substances with a health code of 14 and 15
      Non-serious
        Mild to moderate irritation
    Multiple health codes
      Non-serious
        Until the concentration reaches a level which a serious effect could occur

## Slide 248: Air Contaminant Citations
Documented overexposure
  No violation or citation
    Engineering and/or administrative controls are in place, utilized and effective; and
    Personal protective equipment is provided, utilized and maintained properly
  Example;
    Process evaluated by Professional Engineer (PE) and/or Certified Industrial Hygienist (CIH), documented that engineering controls reduce the contaminant level to lowest possible levels (not below the PEL), and with proper PPE eliminated the hazard to employees.

## Slide 249: Related Citations
General Industry
  29 CFR 1910.94 – Ventilation
  29 CFR 1910.106 – Flammable Liquids
  29 CFR 1910.119 – Process Safety Management of Highly Hazardous Chemicals
  29 CFR 1910.120 – Hazardous Waste Operations and Emergency Response
  29 CFR 1910.123 – 126 – Dipping and Coating Operations
  Subpart I – Personal Protective Equipment
  29 CFR 1910.151 – Medical Services and First Aid
  Subpart Q – Welding, Cutting and Brazing
  Subpart Z – Toxic and Hazardous Substances

## Slide 250: Related Citations
Construction
  29 CFR 1926.20 – General Safety and Health Provisions
  Subpart D – Occupational Health and Environmental Controls
  Subpart E – Personal Protective and Life Saving Equipment
  Subpart J – Welding and Cutting
  Subpart Z – Toxic and Hazardous Substances
  Subpart AA – Confined Spaces in Construction

## Slide 251: Summary
In this course, we discussed
Sampling Equipment
Analytical Techniques
Reasons for Sampling
Sampling Strategies
Evaluation of Sampling Results
The Coburn Equation
Common Citations

## Slide 252: Thank You For Attending!
Final Questions?
1-800-NC-LABOR
(1-800-625-2267)
www.nclabor.com