## Slide 1: Control of Hazardous Energy (Lockout/Tagout) – Part 1
Amputations SEP Training
September 2019
Notes: Rev 3: 7/09/2015
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education, Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.
NCDOL References:
HAZARDOUS ENERGY CONTROL (Lockout/Tagout)
CPL 02-00-147 Control of Hazardous Energy
CPL 02-01-043 Slide-locks-Control of Hazardous Energy
CFR 106 Lockout/Tagout
CFR 106A Lockout/Tagout

## Slide 2: Objectives
Develop a strong & working knowledge the LOTO standard (1910.147) and the documentation needed to support a citation.
Become familiar with the Federal OSHA LOTO CPL and understand how it can be used to support possible citations.
Discuss several accident case studies including those that involve maintenance employees and others where machine operators are involved.

## Slide 3: OSHA LOTO CPL

## Slide 4: OSHA LOTO CPL
CPL 02-00-147, Abstract-3

## Slide 5: If you don’t learn anything else….
CPL 02-00-147, page 3-7

## Slide 6: Lockout/Tagout
Technically known as the Control of Hazardous Energy
  Control of unexpected energization or start-up of machines or equipment, or release of stored energy that could cause injury to employees
1910.147

## Slide 7: Scope – Important Points
This standard protects employees from caught-in or struck-by hazards associated with the unexpected start-up of machinery during servicing and maintenance activities.
It generally does NOT apply to electricians working on the wiring of machinery or the building. That is covered under Subpart S of 29 CFR 1910.
As a result, you should not have an injury of “electrocution” for any 1910.147 citation.

## Slide 8: Subpart S – Electrical Work Practices
1910.333(a)(1) "Deenergized parts." Live parts to which an employee may be exposed shall be deenergized before the employee works on or near them, unless the employer can demonstrate that deenergizing introduces additional or increased hazards or is infeasible due to equipment design or operational limitations. Live parts that operate at less than 50 volts to ground need not be deenergized if there will be no increased exposure to electrical burns or to explosion due to electric arcs.

## Slide 9: Subpart S – Electrical Work Practices
1910.333(b)(2) "Lockout and Tagging." While any employee is exposed to contact with parts of fixed electric equipment or circuits which have been deenergized, the circuits energizing the parts shall be locked out or tagged or both in accordance with the requirements of this paragraph. The requirements shall be followed in the order in which they are presented (i.e., paragraph (b)(2)(i) first, then paragraph (b)(2)(ii), etc.).
  Note 1: As used in this section, fixed equipment refers to equipment fastened in place or connected by permanent wiring methods.
  Note 2: Lockout and tagging procedures that comply with paragraphs (c) through (f) of 1910.147 will also be deemed to comply with paragraph (b)(2) of this section provided that:
  [1] The procedures address the electrical safety hazards covered by this Subpart; and
  [2] The procedures also incorporate the requirements of paragraphs (b)(2)(iii)(D) and (b)(2)(iv)(B) of this section.

## Slide 10: Subpart S – Electrical Work Practices
1910.333(b)(2)(i) "Procedures." The employer shall maintain a written copy of the procedures outlined in paragraph (b)(2) and shall make it available for inspection by employees and by the Assistant Secretary of Labor and his or her authorized representatives.
Bottom Line – Exposures to electrical current need to be addressed under Subpart S and not 1910.147.

## Slide 11: Scope of 1910.147
Covers the servicing and/or maintenance of machines or equipment where the unexpected start-up or release of stored energy could cause injury.
  Servicing and/or maintenance. Workplace activities such as constructing, installing, setting up, adjusting, inspecting, modifying, and maintaining and/or servicing machines or equipment. These activities include lubrication, cleaning or unjamming of machines or equipment and making adjustments or tool changes, where the employee may be exposed to the unexpected energization or startup of the equipment or release of hazardous energy.
1910.147(a)(1)

## Slide 12: Scope – 1910.147
Does not cover
  Construction, agriculture, maritime
  Installations under exclusive control of the electric utilities for power generation, transmission and distribution
  Exposure to electrical hazards from work on, near, or with conductors or equipment in electric-utilization installations
  Oil and gas drilling and servicing
1910.147(a)(1)

## Slide 13: Application
Does not cover:
  Work on cord and plug connected equipment where plug is under exclusive control of employee performing servicing/maintenance
  Hot tap operations, under special conditions
  Normal production operations
1910.147(a)(2)

## Slide 14: CPL Tidbits on Scope/Application
CPL 02-00-147, page 3-17

## Slide 15: CPL Tidbits on Scope/Application
CPL 02-00-147, page 3-3

## Slide 16: CPL Tidbits on Scope/Application
CPL 02-00-147, page 3-3

## Slide 17: CPL Tidbits on Scope/Application
CPL 02-00-147, page 3-4

## Slide 18: Application
Servicing and/or maintenance which takes place during normal production operations is covered by 1910.147 only if:
  Employee is required to remove or bypass a guard or other safety device; or
  Employee is required to place any part of his/her body into the point of operation or where an associated danger zone exists during a machine operation.
1910.147(a)(2)

## Slide 19: What does the CPL say about this?
CPL 02-00-147, page 3-7

## Slide 20: Production or Servicing?
CPL 02-00-147, page 3-7

## Slide 21: Application
Exception
  Minor tool changes and adjustments, and other minor servicing activities, which take place during normal production operations, are not covered if they are:
    Routine,
    Repetitive, and
    Integral to the use of the equipment for production
    …provided that the work is performed using alternative measures which provide effective protection.
1910.147(a)(2)

## Slide 22: Minor Servicing Exemption
CPL 02-00-147, page 3-26

## Slide 23: Minor Servicing Exemption
CPL 02-00-147, page 3-27

## Slide 24: What are Alternative Measures?
CPL 02-00-147, page 3-27

## Slide 25: What are Alternative Measures?
CPL 02-00-147, page 3-28

## Slide 26: Alternative Measures – Example #1
CPL 02-00-147, page 3-29

## Slide 27: Alternative Measures – Example #2
CPL 02-00-147, page 3-30

## Slide 28: Alternative Measures – Example #3
CPL 02-00-147, page 3-30

## Slide 29: Alternative Measures - IMPORTANT
CPL 02-00-147, page 3-31

## Slide 30: Summary of Applicability

## Slide 31: Definitions
Authorized employee
  An employee who locks out or tags out machines or equipment to perform servicing or maintenance on that machine or equipment
  Lockout or tagout is used by these employees for their own protection
1910.147(b)
Authorized

## Slide 32: Definitions
Affected employee
  An employee who performs the duties of his or her job on equipment or in an area in which the energy control procedure is implemented and servicing or maintenance operations are performed
1910.147(b)
Affected

## Slide 33: Other Employees
Other employees
  Other employees whose work operations are, or may be, in an area where energy control procedures may be utilized
1910.147(c)(7)
Other

## Slide 34
Energy source
  Mechanical
  Hydraulic
  Pneumatic
  Electrical
  Kinetic
  Gravity
Definitions
1910.147(b)

## Slide 35: Energy Control Program
The employer shall establish a program consisting of:
  Energy control procedures
  Employee training
  Periodic inspections
1910.147(c)(1)

## Slide 36: Energy Control Program
Important point – there is no requirement for a written LOTO “program.”
Many employers have a generic written LOTO procedure that doesn’t comply with the requirements of 1910.147(c)(4)(ii).
There are requirements for written LOTO components, including:
  Documented energy control procedures (if multiple energy sources or stored energy)
  Certification of periodic inspections
  Certification of employee training

## Slide 37: Energy Control Procedure
Procedures
  Shall be developed, documented and utilized for the control of potentially hazardous energy
  Shall clearly and specifically outline techniques to be utilized to control hazardous energy
1910.147(c)(4)

## Slide 38: Energy Control Procedure
Energy control (LOTO) procedure
  Statement of intended use of procedure
  Steps for shutting down, isolating, blocking and securing machines or equipment to control hazardous energy
  Steps for the placement, removal and transfer of lockout devices or tagout devices and the responsibility for them, and
  Requirements for testing machine/equipment to determine and verify effectiveness of LOTO devices and other energy control measures
1910.147(c)(4)

## Slide 39: Control Sequence
Application of control
  Preparation for shutdown
  Machine or equipment shutdown
  Machine or equipment isolation
  LOTO device application
  Release of stored energy
  Verification of isolation
1910.147(d)

## Slide 40: Written Procedure Exception
    When conducting servicing and/or maintenance on machinery or equipment, an energy control procedure must be developed and utilized, but doesn’t need to be documented if all of the following exceptions apply:
      Machine/equipment has no potential for stored or residual energy after shut down
      Machine/equipment has a single energy source (readily identified and isolated)
      The isolation and locking out of energy source will completely de-energize/deactivate the machine/equipment
      Machine/equipment is isolated from that energy source and locked out during servicing or maintenance
1910.147(c)(4)

## Slide 41: Written Procedure Exception
1910.147(c)(4)
    Lockout device is under the exclusive control of the authorized employee performing the servicing or maintenance
    Servicing/maintenance does not create hazards for other employees; and
    Employer has had no accidents involving the unexpected activation/re-energization of the machine/equipment during servicing/maintenance

## Slide 42: Periodic Inspection
Conducted at least annually to ensure procedure and requirements are followed
Performed by authorized employee other than the one(s) using the procedure
Designed to correct identified deficiencies or inadequacies
Must review each authorized employee’s responsibilities under the energy control procedure
1910.147(c)(6)

## Slide 43: Periodic Inspection
CPL 02-00-147, page 3-65

## Slide 44: Periodic Inspection
CPL 02-00-147, page 3-65

## Slide 45: Periodic Inspection
The employer shall certify that the periodic inspections have been performed. The certification shall identify:
  The machine or equipment on which the energy control procedure was being utilized;
  The date of the inspection;
  The employees included in the inspection; and
  The person performing the inspection.
1910.147(c)(6)(i)

## Slide 46: Training and Communication
Authorized employee
  Recognition of hazardous energy sources
  Type and magnitude of energy in workplace
  Methods and means for energy isolation and control
Affected employee
  Purpose and use of the energy control procedure
1910.147(c)(7)

## Slide 47: Authorized Employee Training
CPL 02-00-147, page 3-61

## Slide 48: Affected Employee Training
CPL 02-00-147, page 3-61

## Slide 49: Affected Employee Training
CPL 02-00-147, page 3-61
Affected Employees must be able to:
This is the training that machine operators who do NOT conduct servicing & maintenance must receive. Your interviews with these employees should focus on these items.
Please note that this is more than “LOTO Awareness” training.
If the operators are unjamming equipment or doing other servicing and /or maintenance work, they must be trained as AUTHORIZED EMPLOYEES.

## Slide 50: Training and Communication
All other employees
  Procedures for energy control
  Prohibition of restarting or reenergizing machines that are locked or tagged out
1910.147(c)(7)
All other employees

## Slide 51: Testing/Positioning Machines
When LOTO devices must temporarily be removed for testing/positioning:
  Clear machine or equipment of tools and materials
  Remove employees from area
  Remove lockout/tagout device
  Energize and proceed with testing or positioning
  Deenergize and reapply energy control measures
1910.147(f)

## Slide 52: Group Lockout/Tagout
When servicing and/or maintenance is performed by a group, they shall utilize a procedure which affords employee protection equivalent to a personal LOTO device
1910.147(f)(3)

## Slide 53: Group Lockout/Tagout
Primary responsibility is vested in an authorized employee
Authorized employee must ascertain exposure status of group members
If more than one crew is involved, a coordinator shall be designated
Each authorized employee shall use a personal LOTO device and remove device when they stop working on machine/equipment
1910.147(f)(3)

## Slide 54: 1910.147 Citations by Frequency (since 2015)

## Slide 55: Keeping it Simple…
The LOTO standard is relatively complicated, but we typically only cite a few main issues:
Failure to develop, document, and/or utilize energy control procedures.
Incomplete energy control procedures.
Inadequate training of authorized or affected employees
Failure to conduct periodic inspections of the procedures and/or authorized employees.
Failure to use group lockout when there are multiple employees doing servicing & maintenance work.

## Slide 56
29 CFR 1910.147(c)(4)(i): Procedures were not developed, documented and utilized for the control of potentially hazardous energy when employees were engaged in the activities covered by this section:

## Slide 57: 1910.147(c)(4)(i) – Lack of ECP
It’s important to first determine which element(s) of this standard have been violated.
  Have energy control procedures been developed? Keep in mind, these procedures could be verbal.
  Have the procedures been documented in writing? Remember, if the machinery and the employer meets all the exceptions (e.g. single energy source, no stored energy, etc.), the procedures don’t have to be documented.
  Are the procedures being utilized by employees during servicing and/or maintenance activities.
Your AVD should outline the specific details – as well as the type of servicing and/or maintenance work that was occurring.

## Slide 58
29 CFR 1910.147(c)(4)(i): Procedures were not developed, documented and utilized for the control of potentially hazardous energy when employees were engaged in the activities covered by this section:
a) Facility – in the Finishing Department where the employer did not develop and utilize machine specific energy control procedures when employees perform servicing and/or maintenance activities on equipment having multiple sources of energy such as but not limited to, the tenter frame SR-1 machine. On or about November 20, 2018, an operator was seriously injured while fixing a machine jam.

## Slide 59
29 CFR 1910.147(c)(4)(i): Procedures were not developed, documented and utilized for the control of potentially hazardous energy when employees were engaged in the activities covered by this section:
b) Laminator Line 3, Horizontal Slitter - where energy control procedures to protect employees from exposure to the Miller Moore slitter 1 (serial number 96238162-004) or slitter 2 (serial number 96238162-003) while performing servicing and maintenance activities, including but not limited to, removing or clearing a jam caused by a material build up, had been developed but were not utilized to clear material jams during production operations.

## Slide 60: Violation Section (B1) – Required Elements
Evidence that must be documented for this citation (and all 1910.147 citations):
  How/why this standard (1910.147) applies. Exactly what servicing and/or maintenance activities were being conducted?
  If during normal production, explain how they had to remove a guard or reach into an associated danger zone.
  Explain how/why the minor servicing exemption does not apply. Is it routine and repetitive? Is the work conducting using alternative measures that provide effective protection?

## Slide 61: Violation Section (B1) – Required Elements
After establishing the standard applies, you need to document how the employer violated its requirements.
  How/why we know procedures were not developed.
  Were the procedures documented in writing? Be sure to explain how the machinery did not meet the exceptions (e.g. multiple energy sources), so the ECP must be in writing.
  Explain how the procedures were not utilized. Be sure to discuss what employees said how they typically handle that servicing and/or maintenance activity.

## Slide 62
29 CFR 1910.147(c)(6)(i): The employer did not conduct a periodic inspection of the energy control procedure at least annually to ensure that the procedure and the requirement of this standard were being followed:
a) facility, routing department - where periodic inspections of the energy control procedures were not conducted for employees performing servicing and/or maintenance activities on equipment such as the C.R. Onsrud Single Table C.N.C. Machine that has multiple sources of energy, to include electrical, hydraulic, and mechanical.

## Slide 63
29 CFR 1910.147(c)(1): The employer did not establish a program consisting of energy control procedures, employee training and periodic inspections to ensure that before any employee performs any servicing or maintenance on a machine or equipment where the unexpected energizing, startup or release of stored energy could occur and cause injury, the machine or equipment was isolated from the energy source and rendered inoperative:
a) facility, where the employer did not implement a lockout/tagout program, including energy control procedures, employee training, and periodic inspections for employees performing servicing and/or maintenance on vertical balers.

## Slide 64
29 CFR 1910.147(c)(7)(i)(A): Authorized employee(s) did not receive training in the recognition of applicable hazardous energy sources, the type and magnitude of the energy available in the workplace, and the methods and means necessary for energy isolation and control:
a) facility, where employees who performed servicing and maintenance on food processing machines, a robotic palletizer and automated shrink wrapper, a case packer, and related equipment had not been trained on the specific procedures for controlling hazardous energy.

## Slide 65
29 CFR 1910.147(c)(4)(ii): Procedures did not clearly and specifically outline the scope, purpose, authorization, rules, and techniques to be utilized for the control of hazardous energy, and the means to enforce compliance including, but not limited to, 29 CFR 1910.147(c)(4)(ii)(A), (c)(4)(ii)(B), (c)(4)(ii)(C) and (c)(4)(ii)(D):
a) within the facility, the employer did not implement lock and tag procedures that outlined specific procedural steps for shutting down, isolating, blocking and securing machines or equipment, placement of lockout devices and verifying the effectiveness of the lock and tag devices for equipment and machinery, such as but not limited to, conveyors, Model 752 packing machine and mixers, which operate at 480 volts.

## Slide 66: Energy Control Procedure
Energy control (LOTO) procedure
  Statement of intended use of procedure
  Steps for shutting down, isolating, blocking and securing machines or equipment to control hazardous energy
  Steps for the placement, removal and transfer of lockout devices or tagout devices and the responsibility for them, and
  Requirements for testing machine/equipment to determine and verify effectiveness of LOTO devices and other energy control measures
1910.147(c)(4)

## Slide 67
29 CFR 1910.147(c)(4)(ii)(B): The energy control procedures did not clearly and specifically outline the specific procedural steps for shutting down, isolating, blocking and securing machines or equipment to control hazardous energy:
a) Dock #23 – where the energy control procedures did not include specific procedural steps to control the hazardous energy associated with gravity on the Kelley dock leveler, Model Number H7X8P, Serial Number 10012121. On July 13, 2016 an employee was crushed beneath the ramp of the dock leveler.

## Slide 68: 1910.147 Citations – Temp Agencies

## Slide 69: Course Continues in Part 2